## Slide 1: IoT/M2M Area Network 物聯網區域網路
國立交通大學資訊工程系
Department of Computer Science
National Chiao Tung University
September 29, 2016
行動寬頻尖端技術跨校教學聯盟
Notes: IoT/M2M 域網

## Slide 2: Outline
Introduction to M2M Area Networks
Example M2M Area Protocols
  ANSI C12 Suite
  Zigbee (IEEE 802.15.4)
  Bluetooth Low Energy (BLE)
Appendix (IoT Devices)
Notes: 大綱
‧介紹M2M區域網
‧ANSI C12 Suite
‧Zigbee
‧BLE/ 藍芽低耗能技術

## Slide 3: Introduction to M2M Area Networks
Notes: 介紹M2M域網

## Slide 4: M2M Area Networks
M2M Devices and Protocols
M2M Applications
Client Applications
M2M
Gateway
M2M Core Network
M2M Area Network
M2M
Network
Service
Capabilities
M2M
Gateway
Service
Capabilities
M2M
Device
Service
Capabilities
M2M Device Domain
M2M Network Domain
M2M Application Domain
Notes: M2M區域網 – 主要M2M設備與通信協定構成

## Slide 5: IoT/M2M Area Network
IoT/M2M Sensors and Devices
  Under fast development!
IoT/M2M Area Network Protocols
  ANSI C12 Suite
  Zigbee (IEEE 802.15.4, 802.15.4e, 802.15.4g)
  Bluetooth Low Energy (BLE)
  WiFi
  Power Line Communication
  BACnet
  KNX
  6LoWPAN/RPL/CoAP
  Etc.
Notes: IoT/M2M 域網
. IoT/M2M 感測器與設備
-正在快速發展中
‧ IoT/M2M 域網協定
. ANSI C12 Suite
. Zigbee
.低功耗藍芽
. Wifi
. Power line Communication
. BACnet
. KNX
. 6LoWPAN/RPL/CoAP

## Slide 6: Catalog of IoT/M2M Sensors (1)
Embedded in Smart Phones
  Accelerometer : Measure the three-axis acceleration
  Magnetic : Measure the magnetic potential vector
  Orientation : Measure the direction
  Gyroscope : Measure the orientation, based on angular momentum (角動量)
  Temperature :Measure the temperature
  Light: Measure the luminosity
  Pressure : Measure the pressure (壓力觸控感測(Force Sensing))
  Proximity : Measure whether any object is closing
  GPS : Positioning the current latitude and longitude
  NFC : Allow smartphones to transfer data to each other within 10 cm
  Etc.
Notes: M2M設備目錄 ( 1 )
‧加速度計：測量三軸加速度。
‧磁性：測量磁向量勢。
‧方向：測量方向。
‧陀螺儀：根據角動量測量方向。
‧溫度：測量溫度。
‧光線：測量光度。
‧壓力：測量壓力。
‧接近：測量是否有對象正在接近。
‧GPS：定位當前的經度和緯度。
‧NFC：允許智慧型手機和相距10 cm內的其它手機進行資料傳輸。
‧紅外線感測器
‧超音波
‧溼度感測器
‧麥克風
‧相機感光元件(CCD)
‧其它

## Slide 7
Catalog of IoT/M2M Sensors (2)
Analogy-hall sensor
磁力感測
Knock sensor
Laser-transmit
Infrared-receiver
Passive buzzer
Push button
Light break sensor
18B20 Temperature Sensor
Active buzzer
Colorful Auto-flash
Infrared-transmitter
Tilt-Switch(傾斜開關)
Notes: . 類比霍爾感測器. 紅外線接收器. 光觸感測器. 彩色自動閃現燈
. 敲擊感測器. 被動蜂鳴器. 溫度感測器 傾斜開關
. 雷射指示器 按鈕 主動蜂鳴器 紅外線傳送器

## Slide 8
Catalog of IoT/M2M Sensors (3)
Magnet-ring sensor
Analog-temperature
sensor
Common-Cathode Red
& Green LED
Rotate-encode
Hydrargyrum-switch
sensor
Hall sensor
Magic-ring
Two-color
Common Cathode (陰極) LED
Humiture sensor
溫濕度感測
Finger-Pulse sensor
Photo resistor sensor
Shock-switch sensor
Notes: . 磁環感測器. 旋轉編碼器. 魔術鈴 手指脈衝感測器
. 類比溫度感測器 汞開關. 雙色共陰極LED 光敏電阻
. 共陰極 紅綠LED 霍爾感測器 溫濕度感測器 衝擊開關

## Slide 9
Catalog of IoT/M2M Sensors (4)
Obstacle avoidance sensor
Microphone sensor
Linear-Hall sensor
Digital-Temperature sensor
Line Tracking sensor
High-Sensitive voice sensor
Metal touch sensor
Flame sensor
Magnetic spring
Notes: . 避障感測器. 跟蹤感測器. 金屬觸碰感測器
. 麥克風感測器 數位溫度感測器. 火焰感測器
. 線性霍爾感測器 高感度聲音感測器 磁力彈簧

## Slide 10
Catalog of IoT/M2M Sensors (5)
Graphic LCD 5110
Ultrasound Sensor
Gas sensor
16 pin LCD module
PIR* sensor
*Passive infrared
Xbee S2 wire antenna
9 gram Plastic Servo Motor
(伺服馬達)
Notes: 超音波感測器 圖型化LCD顯示器 瓦斯感測器 紅外線動作感測器
16 腳位LCD 模組 Xbee 有線天線 6克塑膠伺服馬達

## Slide 11
Catalog of IoT/M2M Sensors (6)
Relay module
Joystick PS2
LED Digitial Indicator
RFID
Card-Reader-Detector
Module
Water level sensor
Stepper motor
(步進馬達)
Notes: 繼電模組 PS2類比搖捍旋紐 LED 數位指示器
RFID 卡片接收器 水位感測器 計步馬達

## Slide 12: Category of Sensor Platforms
NXP JN516x-EK001
Arduino UNO
Intel Galileo
Raspberry Pi
Intel Edison
Mediatek Linkit
Notes: 聯發科Linkit Raspberry Pi Arduino UNO
Intel Edison NXP Intel Galileo

## Slide 13: Catalog of IoT/M2M Devices
Type of IoT/M2M Devices
  Smartphone
  IP camera
  Robot
  Smart Bulb
  E-Lock
  Thermostat
  Smart Watch
  Activity Tracker
  Healthcare
  Etc.
iRobot Roomba 830
Parrot Ar. Drone
Bluetooth Blood Pressure Monitor
Sony Smart Watch
WowWee Rovio
Kwikset Kevo E-Lock
NEST
Honeywell Lyric Thermostat
Dropcam
iPhone
Jawbone UP24
Philips Hue Smart Bulb
Notes: M2M設備目錄 ( 2 )
‧M2M設備類型
–智慧型手機 –IP相機 –機器人 –遊戲機台 –電視遊戲機 –無人地面車輛 –無人航空器
–其它

## Slide 14: Catalog of M2M Area Network Protocols (1)
CoAP/6LoWPAN/RPL
RFID
Bluetooth Low Energy
WiFi
Zigbee (based on IEEE 802.15.4)
Zigbee Smart Energy 2.0
M-Bus – Utility metering
ANSI C12 – Electricity metering
DECT Ultra Low Energy (DECT ULE) (Switzerland)
KNX – HVAC, lighting and building automation
Notes: M2M協定目錄 ( 1 )
.CoAP/6LoWPAN/RPL(IPv6低耗能有損失路由協議)
‧無線射頻辨識 ( RFID )
‧低耗能藍牙( BLE )
‧WiFi
‧IEEE 802.15.4
‧Zigbee* (based on IEEE 802.15.4)
‧Zigbee Smart Energy 2.0
‧M-Bus
‧Insteon
‧ANSI C12
‧KNX
DECT Ultra Low Energy (DECT ULE) is a wireless communication standard used to design wireless sensor and actuator networks for smart home applications.

## Slide 15: Catalog of M2M Area Network Protocols (2)
LonWorks – Control and automation
ModBus – Industry automation and metering
Power Line Communications
BACnet – Building automation and control
Insteon – Smart Home
DLMS/COSEM - Multi utility metering
Z-Wave – Home automation
Dali – Lighting control
X10 - Home automation
DLNA/UPnP – home multimedia sharing
Etc.
Notes: M2M協定目錄 ( 2 )
‧LonWorks
‧ModBus
‧電力線通信 ( PLC )
‧BACnet
‧Insteon
‧DLMS/COSEM
‧Z-Ware
‧Dali
‧X10
.DLNA/UPnP
‧其它

## Slide 16: Example M2M Area Protocols
Notes: 介紹M2M域網

## Slide 17: AnSI C12 Suite
C12.19
C12.18
C12.21
C12.22
RFC 6142
Notes: ANSI C12 Suite

## Slide 18: ANSI C12 Suite
Provide an interoperable solution for data formats, data structures, and communication protocols used in Automatic Metering Infrastructure (AMI) projects and specified by the American National Standards Institute (ANSI).
  C12.01: Code for Electricity Metering
  C12.10: Physical Aspects of Watthour Meters – Safety Standard
  C12.18: Protocol Specification for ANSI Type 2 Optical Port
  C12.19: American National Standard for Utility Industry End Device Data Tables
  C12.20: Electricity Meters – 0.2 and 0.5 Accuracy Classes
  C12.21: Protocol Specification for Telephone Modem Communication
  C12.22: Protocol Specification for Interfacing to Data Communication Networks
  RFC 6142: ANSI C12.22, IEEE 1703, and MC12.22 Transport over IP
Notes: 一套ANSI C12
‧美國國家標準局所制定，提供自動量測設施(AMI)計畫中彼此作用所規定的資料格式，資料結構和同訊協定。
  C12.01: 電力量測編碼
  C12.10: 瓦特‧小時量測的物理觀點 – 安全的標準
  C12.18: ANSI Type2 光學埠通訊協定定義
  C12.19: 為公用事業終端裝置資料表制定之美國國家標準
  C12.20: 電力量測表 – 0.2和0.5準度層級
  C12.21: 電話數據通訊之通訊協定定義
  C12.22: 資料通訊界面網路之通訊協定定義
  RFC 6142: ANSI C12.22，IEEE 1703和 MC12.22透過IP傳輸

## Slide 19: A Brief History
C12.18 (First release published in 1996 then revised in 2006)
  The first standardized protocol that was specified to interact with ANSI C12.19 Data Tables
  Define the communications between a C12.18 meter and a C12.18 client by means of an optical port
C12.19 (1990s published ,2007 revised)
  The standard data structure is specified in the ANSI C12.19 document.
C12.21 (1999)
  Specify the communications between a C12 device and C12 client via a modem
  The first solution for AMI projects
C12.22 (2007)
  Allow interactions with C12.19 table data over any networking communications system
RFC 6142 (2011)
  Propose a framework for transporting ANSI C12.22 Application Layer messages on an IP network
Notes: 簡單回顧
‧C12.19(1990s發表, 2007修訂)
- 被定義在ANSI C12.19文件的標準資料結構
‧C12.18
- 第一個版本在1996年發表，然後在2006年修訂
‧C12.21(199)
- 確立C12裝置和C12客戶間透過數據機的通訊
‧C12.22(2007)
- 允許透過任何網路通訊系統和C12.18的資料表互動
‧RFC 6142(2011)
- 提出在IP層上傳輸ANSI C12.22應用層訊息的架構

## Slide 20: Network Protocol Stack
C12.19
(Data Model)
C12.18
Application
Presentation
Session
Transportation
Network
Data Link
Physical
C12.21
C12.18
(Optical)
C12.21
(Modem)
Request-Response
Model
RFC 6142
C12.22
Notes: 網路協定層級

## Slide 21: C12.19: The Data Model
Defines a data structure for representing metering data and metering functions exposed by a metering equipment to a client machine.
  The data structure is defined as a set of standard tables.
  Besides standard tables, C12.19 also provides a standard way to add proprietary tables called manufacturer tables.
Does not specify data transport protocol.
Notes: C12.19: 資料模組
‧定義一個代表提供給使用者測量資料和測量功能的資料結構。
- 資料結構被一組標準表所定義
- 除了標準表，C12.19也提供了標準方法去新增叫做製造商表的所有權表
‧沒有包含任何傳輸資料的協定。

## Slide 22: Decade
Tables that share a common purpose or are relative to a common feature are called a “decade”.
  There are 17 decades in the version published in 2007.
Decade number | Name of the Decade | # of Tables in the Decade | Decade number | Name of the Decade | # of Tables in the Decade | Decade number | Name of the Decade | # of Tables in the Decade
0 | Configuration Tables | 9 | 6 | Load Profile Tables | 8 | 12 | Network Control Tables | Defined in ANSI C12.22
1 | Data Source Tables | 9 | 7 | History & Events Logs | 10 | 13 | Relay Control Tables | Defined in ANSI C12.22
2 | Register Tables | 9 | 8 | User-Defined Tables | 10 | 14 | Extended User Defined Tables | 4
3 | Local Display Tables | 5 | 9 | Telephone Control Tables | 9 | 15 | Quality of Service Tables | 9
4 | Security Tables | 7 | 10 | Extended Source Tables | 4 | 16 | One-Way Tables | 5
5 | Time-of-Use Tables | 7 | 11 | Load Control & Pricing Tables | 9 |  |  | 
Notes: 分享普遍目的或關於一般特徵的表被稱作”decade”
- 2007發表的版本有17個decades

## Slide 23: Read/Write Services
The read service request allows the transfer of table data from a sending party to a receiving party.
  Full table read: specified by Table_Identifier
  Partial table read
    Index-based: specified by up to 5 indexes and optionally an element count
    Offset-based: specified by an offset and optionally a count
The write service allows unsolicited data to be sent to a receiving party.
  Support both full and partial table write
Notes: 讀/寫 服務
‧讀服務的要求允許從一個寄送群體傳遞關於表的資料到接受群體。
- 完整的表讀取: 由Table_Identifier指定
- 部分的表讀取:
‧索引基準: 由多達五個索引和一個元素個數值(選擇性)
‧偏移基準: 由一個偏移植和一個元素個數值
‧寫的服務允許不請自來的資料被送到接受群體
- 支援包括完整和部分的表寫入

## Slide 24: Three Remarkable Tables in Decade 0
Table 00 (GEN_CONFIG_TBL)
  The information related to the configuration of the end device
  E.g., the list of supported tables and procedures
Table 07 and Table 08 are designed for enabling the execution of commands
  Procedure Initiate Table: an initiator writes parameters in the Table 07 to execute a command in a meter
  Procedure Response Table: the result is placed in Table 08 to be read by the initiator
  No buffering: only one command at a time
  “If a procedure initiate request is followed by another procedure initiate request, the procedure response for the first procedure initiate request may be lost.”
Notes:   28 standard procedures that may be executed by using Tables 07 and 08 are defined, including cold start, warm start, save configuration, remote reset, set date and/or time, execute diagnostics, etc.
  有28個標準過程通過使用表07和08來執行，包含冷啟動，熱啟動，保存配置，遠程復位，設置日期和/或時間，執行診斷等等。
  Decade 0 中三個卓越的表
  ‧Table00 (GEN_CONFIG_TBL)
  - 有關終端裝置設定的資料
  - 例如支援的表和程序的清單
  ‧Table07和Table08被設計來能夠執行指令
  - 初始程序表: 一個在測量錶中寫參數進Table07去執行指令的初始者
  - 程序回復表: 結果被放置在Table08且被初始者讀取
  - 沒有緩衝: 同時只有一個指令
  “如果一個程序初始需求皆在其他程序的初始需求之後，第一個程序初始需求的程序回復可能會遺失”

## Slide 25: C12.18: Basic Point-to-Point Communication over an Optical Port
The communications between an electric metering equipment and another client device via an optical port
  The first standardized protocol that was specified to interact with ANSI C12.19 Data Tables
  Focuses on the physical, data link and application layers
Three main functionalities
  Modification of the communication channel;
  Transport of information to and from the metering device;
  Closure of the communication channel when communications are complete.
Notes: C12.18: 光學埠基本點對點傳輸
‧透過光學埠電表裝置和其他客戶端裝置間的通訊
- 第一個詳細說明和ANSI C12.19資料表互動的標準化的協定
- 著重在物理、資料連結和應用層
‧三個主要的功能
- 修改通訊頻道
- 輸送資訊到/從量測裝置
- 當通訊完成後關閉通訊頻道

## Slide 26: Protocol Specifications for Electric Metering (PSEM)
The application layer defines the PSEM language
  Provide basic services for channel configuration and information retrieval
  Use request–response scheme
Provides settings for Layer-2 and Layer-1 establishment
  E.g., baud rate, number of packets, packet size channel traffic time-out, data type, data format and data polarity
Nine services are defined in PSEM, including
  Identification service
  Read service
  Write service
  Logon service
  Security service
  Logoff service
  Negotiate service
  Wait service
  Terminate service
Notes: 電力量測協定的詳細說明
‧應用層定義了PSEM語言
- 提供頻道測定和資訊取回的基本服務
- 使用要求-回復的架構
‧提供第二層和第一層建立的設定
- 舉例來說，傳輸速率、封包數、封包大小頻道交通暫停時間、資料類型、資料格式和資料兩極
‧九種服務被定義在PSEM，包括
- 識別服務
- 讀服務
- 寫服務
- 登入服務
- 安全服務
- 登出服務
- 協商服務
- 等待服務
- 結束服務

## Slide 27: C12.21: An Extension of C12.18 for Modem Communication
Allows remote interactions with ANSI C12.19 tables over a telephone network.
The three main functional areas specified in the C12.18 are not modified.
Instead of 9 services specified in the C12.18, the PSEM provides 12 services.
  7 services are identical: read, write, logon, security, logoff, negotiate, wait.
  2 services are modified: identification and terminate.
  3 new services are provided: timing setup, disconnect, and authenticate.
Notes: C12.21: C12.18用於當代通訊的增加部分
‧可透過電話網路和ANSI C12.19表做遠端互動
‧被詳細說明在C12.18的主要三個功能區域沒有被修改
‧除了九個被說明在C12.18外，PSEM提供了十二項服務
- 七個服務相似: 讀、寫、登入、安全、登出、協商、等待
- 兩個服務被修改: 識別和結束
- 三個新的服務被提供: 計時設定、中斷連接和認證

## Slide 28: Interactions with the Data-Link Layer
The communication channel of the modem is established with a set of default parameters.
After calling the identification service and before calling the logon service, the service layer can
  Call either the negotiate service or the Timing_Setup service
  Modify packet size, packet number for reassembly, timers, or retry attempts number.
Notes: 和資料連結層互動
‧數據機的通訊頻道建立時有一組預設的參數
‧呼叫識別服務之後和呼叫登入服務之前，服務層可以
- 透過呼叫協商服務或者計時設定服務
- 修改封包大小、重新組成資料的封包數，或重試想要的數值

## Slide 29: Modifications and Additions to C12.19 Tables
The most significant changes to C12.19 tables includes
  The Procedure Initiate Table (Table 07) was modified to add a new standard procedure in order to trigger an immediate call establishment with a phone number specified as a procedure parameter
  A new decade (no. 9) that contains 7 new tables associated with the use of a telephone modem.
Notes: C12.19表的修改和新增項目
‧C12.19表最重要的改變包括
- 程序初始表(Table 07)為了觸發和程序參數指定的電話號碼立即建立呼叫而增加了一個標準程序
- 新的decade(no. 9)包含了七個新的有關電話數據機使用的表

## Slide 30: C12.22: Enable Transportation over any Networking Communication System
Defines several types of network elements that are used in a reference topology
Describes interfaces between different types of network elements
New data tables are added and some existing tables are also modified
Notes: C12.22: 允許透過任何網路通訊系統傳輸
‧定義了使用在相關拓樸的幾種網路元素類型
‧描述不同網路元素類別間的介面
‧新增新的資料表，且一些已經存在的表也被修改

## Slide 31: C12.22 Reference Topology
Source: ANSI C12.22, Chapter 5, Figure 5.1; The Internet of Things
Notes: C12.22 參考拓樸

## Slide 32: Network Elements in C12.22 (1/2)
C12.22 Host: this is a termination point in a C12.22 network. It may be an authentication host or/and notification host.
C12.22 Device: this is a network element that contains a C12.22 application.
C12.22 Communication Module: this is a hardware device that allows communications between a C12.22 Device and a C12.22 network.
C12.22 Node: it is a combined C12.22 communication-module/device network element.
Notes: C12.22中的網路元素
‧C12.22 主機: 一個C12.22網路的結束點。他可能是個認證主機 和/或 通知主機
‧C12.22 裝置: 一個包含C12.22應用的網路元素
‧C12.22 通訊模組: 讓C12.22裝置和C12.22網路彼此通訊的硬體裝置
‧C12.22 節點: 由C12.22 通訊模組和裝置結合成的網路元素

## Slide 33: Network Elements in C12.22 (2/2)
C12.22 Master Relay:
C12.22 Relay:
  This layer 7 address is called ApTitle (application process title)
C12.22 Gateway: this is a protocol converter from the C12.22 protocol to any other protocol.
Notes: C12.22中的網路元素
‧C12.22 主繼電器:
‧C12.22 繼電器:
- 這個第七層地址被稱作ApTitle(應用處理標題)
‧C12.22 閘道器: 從C12.22協定轉換到其他協定的協定轉換器

## Slide 34: C12.22 Node to C12.22 Network Communications
The protocol stack between a C12.22 node and a C12.22 network is only defined at layer 7.
The new version of the PSEM protocol contains 13 services:
  Three services are unchanged: the read, write and security services.
  Six services are modified (compared to C12.21): identification, logon, logoff, terminate, disconnect, and wait services.
  Four new services are provided: registration, deregistration, resolve, and trace services.
The extended PSEM (EPSEM) is specified to allow sending multiple requests and receiving multiple responses simultaneously.
C12.22 security mechanism supports both authentication and encryption
Notes: C12.22節點到C12.22網路的通訊
‧C12.22節點和C12.22網路間的通訊堆疊只被定義在七層
‧新版本的PSEM協定包含了13種服務:
- 三個服務沒被改變: 讀、寫和安全服務
- 六個服務被改變(比較C12.21):
- 四個新的服務被提供: 註冊、註銷、分解、追蹤服務
‧延伸的PSEM(EPSEM)被用來同時送多個要求和接收多個回覆
‧C12.22安全機制支援認證和加密

## Slide 35: C12.22 Communication Module
The concept of C12.22 communication modules is introduced to model the communication ports of C12.22 meters.
  Connects to the C12.22 Device through an interface defined in the C12.22 standard.
  Connects to any LAN (e.g., ZigBee, …), WAN (DSL, GPRS, …), or MAN (Ethernet, …).
Source: The Internet of Things, Chapter 10, Figure 10.1.
Notes: C12.22 通訊模組
‧C12.22通訊模組的觀念被引用來建C12.22測量錶的通訊埠的模型
- 透過C12.22標準定義的介面連接到C12.22裝置
- 連到任何區域網路(ZigBee,…)，廣域網路(DSL,GPRS,…)或者城域網路(Ethernet,…)

## Slide 36: C12.22 Protocol Stack and Services
Source: The Internet of Things, Chapter 10, Figure 10.3.
Transport Layer Service
Negotiate service
Get-Configuration service
Link-Control service
Send-Message service
Get-Status service
Get-Registration-Status service
Notes: C12.22 協定推疊和服務
傳輸層服務
.協商服務
.取得配置服務
.鏈路控制服務
.發送消息服務
.獲取狀態服務
.讀取註冊狀態服務

## Slide 37: C12.19 Updates
Decade 12 “Node Network Control Tables” is added, modeling the C12.22 node access to a C12.22 network
Decade 13 “Relay Control Tables” is added, related with the management of a C12.22 relay.
The content of the Procedure Initiate Table is augmented with 4 new procedures (Registration, Deregistration, Network Interface Control, and Exception Report), related to the newly added Decade 12
Notes: C12.19更新
‧Decade 12 加入“節點網路控制表”，將C12.22節點進入C12.22網路模組化
‧Decade 13 加入”繼電器控制表”，C12.22繼電器的控制有關
‧程序初始表的內容擴大到四個程序(註冊、註銷、網路介面控制和例外報告)，和新增的Decade 12有關

## Slide 38: RFC 6142: C12.22 Transport Over an IP Network
Transport C12.22 messages by using TCP and UDP transports over an IP network.
  Specifies an encoding for the native IP address in the appropriate fields of ANSI C12.19 Tables.
    IPv4 and IPv6 are two possible options.
  Port number 1153 was assigned by IANA* for both TCP and UDP.
Since C12.22 has its own security mechanism, transport layer security is not mandated. RFC 6142 allows the use of a transport layer security mechanism as an enhancement.
*IANA: Internet Assigned Number Authority
Notes: RFC 6142: C12.22傳輸透過IP網路
‧用TCP和UDP傳輸C12.22訊息透過IP網路
- ANSI C12.19表適當的欄位中原本的IP地址確定一種編碼系統
‧IPv4和IPv6是兩種可能的選項
- 編號1153的埠被IANA分配給TCP和UDP
‧因為C12.22有它自己的安全機制，傳輸層安全沒有被規定。RFC 6142允許傳輸層安全機制的使用以做強化
IANA : 國際號碼分配局

## Slide 39: RFC 6142: C12.22 Transport Over an IP Network (Cont.)
To facilitate the reading of numerous C12.22 meters, the support of IP multicast is required in all C12.22 hosts, relays and master relays and recommended in the C12.22 nodes.
  Meters with a common C12.22 multicast group ApTitle can be reached by sending a single EPSEM read request.
  224.0.2.4 for IPv4 and FF0X::24 for IPv6 have been assigned by IANA to a newly created “All C1222 Nodes” multicast group.
  TTL (Time To Live) attribute in an IP packet header is used to limiting the propagation of C12.22 IP multicast messages.
Notes: ‧為了使讀取許多的C12.22錶容易，C12.22主機們需要支援IP多播，C12.22節點建議有繼電器和主繼電器
- 普遍的C12.22多播群組ApTitle藉由送單一個EPSEM讀取需求可以被做到
- IPv4的224.0.2.4和IPv6的FF0X::24被IANA分配給新產生的”All C1222 Nodes”多播群組
- IP 封包標頭中的TTL(Time To Live) 屬性被用來限制C12.22 IP多播訊息的增殖

## Slide 40: ZigBee
Notes: ZigBee

## Slide 41: ZigBee
ZigBee is a standardized wireless protocol for personal area networking, or “WPAN.”
The protocol is the work and property of the ZigBee Alliance, a consortium that creates and promotes this WPAN standard
ZigBee is built on IEEE 802.15.4 standard that defines physical (PHY) and Medium Access Control (MAC) layers of a WPAN.
The ZigBee Alliance defines Network (NWK) and Application (APL) layer specifications to complete what is called the ZigBee stack.
Designed for low cost, low power, low data rate, low duty cycle wireless connectivity.
Notes: ZigBee
. ZigBee是用於個人區域網絡的標準化無線協議，或“WPAN”。
. 該協議是ZigBee聯盟的努力成果，ZigBee是創建和促進該WPAN標準的聯盟
. ZigBee建立在定義WPAN的實體（PHY）和媒體接入控制（MAC）層的IEEE 802.15.4標準上。
. ZigBee聯盟定義網絡（NWK）和應用（APL）層規範以完成所謂的ZigBee層。
. 專為低成本，低功耗，低數據速率，低佔空比無線連接而設計。

## Slide 42: ZigBee/802.15.4 architecture
ZigBee Alliance
  45+ companies: semiconductor mfrs, IP providers, OEMs, etc.
  Defining upper layers of protocol stack: from network to application, including application profiles
  First profiles published mid 2003
IEEE 802.15.4 Working Group
  Defining lower layers of protocol stack: MAC and PHY
PHY Layer
MAC Layer
Network&Security Layer
Application framework
Application profiles
Application
802.15.4
ZigBee alliance
Hardware
ZigBee stack
Application
ZigBee/802.15.4 architecture
Notes: 介紹802.15.4以及ZigBee的架構，圖為表示802.15.4主要是作用在MAC以及PHY層的協定，而ZigBee則作用在很多層之間

## Slide 43: ZigBee Applications
Source: https://www.nxp.com/files/training_pdf/28081_ZIGBEE_OVERVIEW_WBT.pdf
HVAC: Heating, ventilation, and air conditioning
Notes: ZigBee 應用
. 建築自動化
. 個人健康照顧
. 工業控制
. 電力消耗
. 電腦周邊設備
. 燈光及商業控制

## Slide 44: ZigBee Market Goals
Global band operation, 2.4 GHz unlicensed band or one of the 900MHz regional bands
Unrestricted geographic use
RF penetration through walls and ceilings
Automatic or semi-automatic installation
Easy to add or remove devices
Low cost
Notes: ZigBee 市場上目標
. 全域頻段操作，2.4 GHz無執照頻段或900MHz區域頻段之一
. 不受限制的地理使用
. RF穿透牆壁和天花板
. 自動或半自動安裝
. 容易添加或刪除設備
. 低成本

## Slide 45: ZigBee Technical Specs
Data throughput: 10 kbps to 115 kbps
Range: 10 to 75 m coverage
Scalability: Up to 100 collocated networks
  Each network could have up to 1000 nodes in practice
Low power: Up to 2 years of battery life on standard alkaline batteries
Notes: ZigBee 技術規範 . 數據吞吐量：10 kbps至115 kbps
. 範圍：10到75米覆蓋
. 可擴展性：最多100個並置網絡
. 低功耗：標準鹼性電池可長達2年的電池壽命

## Slide 46: ZigBee Network Models
RFD: Reduced Function Device
FFD: Full Function Device
Coordinator: A full function device that manages the network.
Source: https://www.nxp.com/files/training_pdf/28081_ZIGBEE_OVERVIEW_WBT.pdf
Notes: ZigBee 網絡模型
RFD：精簡功能器件
FFD：全功能設備
協調器：管理網絡的全功能設備

## Slide 47: Components
PAN coordinator (ZigBee coordinator)
  Main controller of a PAN
  A network has exactly one PAN coordinator
Coordinator (ZigBee router)
  Provide synchronization services through the transmission of beacons
Device (ZigBee end device)
  Any entity w/ IEEE 802.15.4 MAC and PHY interface
Notes: ZigBee擁有coordinator以控制PAN，且具有同步功能

## Slide 48: ZigBee Network Topology

## Slide 49: Network Topologies (cont’d)
Cluster Tree Topology
Cluster
Head
CID 1
CID 3
CID 2
CID 5
CID 4
PAN Coordinator
PAN
Coordinator
Cluster ID 0
Notes: 群及樹狀拓墣

## Slide 50: ZigBee Network Topology
Notes: 不同拓僕的優缺點

## Slide 51: IEEE 802.15.4 Device Types
Network Coordinator
  Maintains overall network knowledge; most sophisticated of the three types; requires most memory and computing power
Full Function Device (FFD)
  Carries full 802.15.4 functionality and all features specified by the standard
  Additional memory, computing power make it ideal for a network router function
  Could also be used in network edge devices where the network touches other networks or devices that are not IEEE 802.15.4 compliant
Reduced Function Device (RFD)
  Carriers limited (as specified by the standard) functionality to control cost and complexity
  General usage will be in network edge devices
Notes: .網絡協調器
-維護整體網絡知識; 最複雜的三種類型; 需要大多數內存和計算能力
.全功能設備（FFD）
-具有完整的802.15.4功能和標準規定的所有功能
-額外的記憶體，計算能力使其成為網絡路由器功能的理想選擇
-亦可用於網絡邊緣設備，其中網絡接觸不符合IEEE 802.15.4標準的其他網絡或設備
.簡化功能設備（RFD）
-載波限制（由標準規定）功能來控制成本和複雜性
-一般使用將在網絡邊緣設備

## Slide 52: ZigBee Protocol Stack
Source: https://www.nxp.com/files/training_pdf/28081_ZIGBEE_OVERVIEW_WBT.pdf
Notes: ZigBee 協定層

## Slide 53: IEEE 802.15.4 Standard Basics
CSMA channel access with collision avoidance and optional time slotting
Three bands, 27 channels specified
  2.4 GHz: 16 channels, 250 kbps
  868.3 MHz : 1 channel, 20 kbps
  902-928 MHz: 10 channels, 40 kbps
Message acknowledgment for improved data delivery reliability
Beacon structures to improve latency.
Multi-level security
Designed for monitoring and control applications where battery life is important. 802.15.4 is the source of ZigBee’s excellent battery life.
Channel 0
868.3 MHz
Channel 1-10
2 MHz
902 MHz
928 MHz
Channel 11-26
2.4 GHz
PHY
2.4 GHz
2.4835 GHz
Notes: IEEE 802.15.4標準基礎
. 具有衝突避免和可選時隙的CSMA信道接入
. 三個頻段，指定27個頻道
-2.4GHz：16個信道，250kbps
-868.3MHz：1信道，20kbps
-902-928MHz：10個信道，40kbps
. 消息確認，以提高數據傳輸可靠性
. 信標結構，以改善延遲。
. 多層級安全
. 專為監控和控制電池壽命很重要的應用而設計。 802.15.4是ZigBee優秀電池壽命的源泉。

## Slide 54: IEEE 802.15.4 MAC Features
Employs 64-bit IEEE & 16-bit short addresses
  Ultimate network size can be 264 nodes (more than probably needed)
  Using local addressing, simple networks of more than 65,000 (216) nodes can be configured, with reduced address overhead
Simple frame structure
Reliable delivery of data
Supports AES-128 security
Employs CSMA-CA channel access for better coexistence
Offers optional superframe structure for improved latency
Notes: . 採用64位IEEE和16位短地址
-終極網絡大小可以是264個節點（可能需要更多）
-使用本地尋址，可以配置超過65,000（216）個節點的簡單網絡，減少地址(address)開銷
. 簡單的訊框結構
. 可靠的數據交付
. 支持AES-128安全性
. 實施CSMA-CA信道接入以實現更好的共存
. 提供可選的superframe結構，以改善延遲

## Slide 55: IEEE 802.15.4 MAC Options
Non-beacon network
  Standard ALOHA CSMA-CA communications
  Positive acknowledgment for successfully received packets
Optional beacon-enabled network
  Superframe structure
    For dedicated bandwidth and low latency
    Set up by network coordinator to transmit beacons at predetermined intervals
      » 15ms to 252sec (15.38ms ∗ 2n where 0 ≤ n ≤ 14)
      » 16 equal-width time slots between beacons
      » Channel access in each time slot is contention free
Notes: . 非信標網絡
-標準ALOHA CSMA-CA通信
-成功接收數據包的肯定確認
. 可選的啟用信標的網絡
-Superframe結構
。用於專用帶寬和低延遲
。由網絡協調器設置，以預定的時間間隔傳輸信標
»15ms至252sec（15.38ms * 2n，其中0≤n≤14）
»信標之間有16個等寬時間間隔
»每個時隙中的信道訪問是不用爭奪的

## Slide 56: 802.15.4 Data Frame Packet
Provides up to 104 byte data payload capacity
PHY Service Data Unit (PSDU) is a maximum of 127 bytes in length
Data sequence numbering ensures that packets are tracked
Robust structure improves reception in difficult conditions
Frame Check Sequence (FCS) validates error-free data
Source: https://www.nxp.com/files/training_pdf/28081_ZIGBEE_OVERVIEW_WBT.pdf
Notes: PLCP: Physical Layer Convergence Protocol
PPDU: PLCP Protocol Data Unit (wireless LANs)
.提供高達104字節的數據有效負載容量
.PHY服務數據單元（PSDU）的長度最大為127字節
.數據序列編號確保追蹤數據包
.堅固的結構改善了在困難條件下的接收
.訊框檢查序列（FCS）驗證無錯誤數據

## Slide 57: 802.15.4 Acknowledgment Frame Format
The acknowledgment frame, or ACK, confirms that the data is received successfully.
Frame control and Data sequence are taken from the original packet.
A transmission is considered successful if the ACK frame contains the same sequence number as the transmitted frame.
Source: https://www.nxp.com/files/training_pdf/28081_ZIGBEE_OVERVIEW_WBT.pdf
Notes: 訊框(frame)確認或ACK確認數據已成功接收。
訊框控制和數據序列取自原始分組。
如果訊框ACK包含與所發送的訊框相同的序列號，則認為發送是成功的。

## Slide 58: 802.15.4 Command Frame Format
The command frame is used for remote control. Instead of data as the
payload, this frame contains command information. A command type byte is
added as well. The MPDU must still be 127 bytes or less as with the Data
frame.
Source: https://www.nxp.com/files/training_pdf/28081_ZIGBEE_OVERVIEW_WBT.pdf
Notes: 指令訊框用於遠程控制。 而不是當作內容(payload)的數據，該訊框包含命令信息。
也會添加指令類型的字節(byte)。 與資訊訊框一樣，MPDU必須仍然為127或更少的字節。

## Slide 59: Frame Control
Octets:2 | 1 | 0/2 | 0/2/8 | 0/2 | 0/2/8 | 0/5/6/10/14 | Variable | 2
Frame Control | Sequence Number | Dest. PAN Identifier | Dest. Address | Source PAN Identifier | Source Addr. | Auxiliary Security Header | Frame Payload | FCS
Bits: 0-2 | 3 | 4 | 5 | 6 | 7-9 | 10-11 | 12-13 | 14-15
Frame Type | Security Enabled | Frame Pending | Ack Request | PAN ID Compre-ssion | Reserved | Dest. Addr. Mode | Frame Version | Source Addr. Mode
Notes: 其中MHR 中的訊框控制欄位的長度為16位，共分為訊框(Frame)類型、安全致能、資料待傳、確認請求、網內/網際、目的位址模式、來源位址模式及保留跟訊框(Frame)版本等9個子域。

## Slide 60: Frame Control Field

## Slide 61: Individual Frame Format
Octets:2 | 1 | 4/10 | 0/5/6/10/14 | 2 | variable | variable | variable | 2
Frame Control | Sequence Number | Addressing fields | Auxiliary Security Header | Superframe Specification | GTS fields | Pending address fields | Beacon Payload | FCS
MHR |  |  |  | MAC Payload |  |  |  | MFR
Beacon frame format
Octets:2 | 1 | (see7.2.2.2.1) | 0/5/6/10/14 | variable | 2
Frame Control | Sequence Number | Addressing fields | Auxiliary Security Header | Data Payload | FCS
MHR |  |  |  | MAC Payload | MFR
Data frame format
000
001

## Slide 62: 802.15.4 Beacon Frame Format
The beacon frame is much more complex as it must convey the synchronization
and guaranteed time slot (GTS) information to all of the devices in the network.
Beacons add a new level of functionality to a network. Client devices can wake up
only when a beacon is to be broadcast, listen for their address, and if hear nothing,
return to sleep.
Beacons are important for mesh and cluster tree networks to keep all of the nodes
synchronized without requiring nodes to consume precious battery energy listening
for long periods of time.
Source: https://www.nxp.com/files/training_pdf/28081_ZIGBEE_OVERVIEW_WBT.pdf
Notes: .信標(Beacon)訊框要復雜得多，因為它必須傳送同步和保證時隙（GTS）信息到網絡中的所有設備。
.Beacons為網絡增加了一個新的功能級別。 僅當要廣播信標時，客戶端設備可以醒來，監聽他們的地址，並且如果聽不到任何聲音，再回到睡眠。
.信標對於網格和集群樹網絡保持所有節點的同步是重要的，而不需要節點長時間消耗寶貴的電池能量。

## Slide 63: Individual Frame Format (cont’d)
Acknowledgement frame format
MAC command frame format
Octets:2 | 1 | 2
Frame Control | Sequence Number | FCS
MHR |  | MFR
Octets:2 | 1 | (see7.2.2.4.1) | 0/5/6/10/14 | 1 | variable | 2
Frame Control | Sequence Number | Addressing fields | Auxiliary Security Header | Command Frame Identifier | Command Payload | FCS
MHR |  |  |  | MAC Payload |  | MFR
010
011

## Slide 64: 802.15.4 Command Frame Format
Command frame identifier | Command name
0 x 01 | Association request
0 x 02 | Association response
0 x 03 | Disassociation notification
0 x 04 | Data request
0 x 05 | PAN ID conflict notification
0 x 06 | Orphan notification
0 x 07 | Beacon request
0 x 08 | Coordinator realignment
0 x 09 | GTS request
0x0a～0xFF | Reserved
Notes: 0x01為關聯請求，投影片 p.47
0x02為關聯回應，投影片 p.47
0x03為解關聯通知，投影片 p.48
0x04為資料請求，投影片 p.64-65
0x05為PAN ID衝突通知，有時候設備不只會聽到一個PAN的信標(Beacon)，設備會去比較每個信標裡的PAN ID是否衝突，當設備檢測到PAN ID衝突時，就向PAN協調器發出PAN ID衝突通知命令。
0x06為孤立通知，當一個設備和它的協調器失去同步時，就發出孤立通知命令。
0x07為信標請求，信標請求命令由設備主動向範圍內所有協調器請求信標。
0x08為協調器重排列，當系統收到其PAN中的孤立設備發出的孤立通知命令，就發出協調器重排列命令。
0x09為GTS請求，GTS請求可以向PAN協調器請求分配一個新的GTS或撤銷一個現存的GTS。
其他為保留

## Slide 65: Association
If device wait a aResponseWaitTime and no any Association response, then Association failure
Coordinator MAC
Device
MAC
Association request
ACK
aResponseWaitTime
Data
request
ACK
Association response
ACK
Beacon
Append device’s
long address in beacon
Notes: 裝置向協調者發出關聯請求Association request
，而協調者回應關聯請求命令確認訊框 ack，假使裝置收到關聯請求回應命令確認訊框後ack，裝置最多在aResponseWaitTime的時間(因為是競爭模式)
之後會嘗試向協調器要求關聯回應命令Association response
，如果裝置不能從協調器獲得關聯回應命令訊框Association response
，則關聯嘗試失敗。
資料來源http://standards.ieee.org/getieee802/download/802.15.4-2003.pdf (p80)
An unassociated device shall initiate the association procedure by sending an associate request command
(see 7.3.1.1) to the coordinator of an existing PAN. If the association request command is received correctly,
the coordinator shall send an acknowledgment frame, thus confirming receipt.
The acknowledgment to an association request command does not mean that the device has associated. The
coordinator needs time to determine whether the current resources available on the PAN are sufficient to
allow another device to associate. The coordinator shall make this decision within aResponseWaitTime
symbols. If the coordinator finds that the device was previously associated on its PAN, all previously
obtained device-specific information shall be removed. If sufficient resources are available, the coordinator
shall allocate a short address to the device and generate an association response command (see 7.3.1.2)
containing the new address and a status indicating a successful association

## Slide 66: Association
In IEEE 802.15.4, association results are announced in an indirect fashion.
  A coordinator responds to association requests by appending devices’ long addresses in beacon frames
Devices need to send a data request to the coordinator to acquire the association result
After associating to a coordinator, a device will be assigned a 16-bit short address.
Notes: 而協調者回應關聯請求命令在beacon frames 通過devices長位址
關聯到一個協調者後，設備將被分配一個 16位的短位址

## Slide 67: ZigBee Architecture Objectives
Support all target environments and applications that are in the scope of ZigBee:
  Ensure that devices are efficient in their use of the available bandwidth
Provide a platform and implementation for wirelessly networked devices:
  Make it easy to design and develop ZigBee devices
  Reduce today’s cost of building wireless solutions
Ensure interoperability through the definition of application profiles
  Enable out-of-the-box interoperable devices where desired by manufacturers
Source: https://www.nxp.com/files/training_pdf/28081_ZIGBEE_OVERVIEW_WBT.pdf
Notes: .支持ZigBee範圍內的所有目標環境和應用程序：
- 確保設備在使用可用帶寬方面高效
.為無線網絡設備提供平台和實施：
- 易於設計和開發ZigBee設備
- 降低當今建設無線解決方案的成本
.通過定義應用程序配置文件確保互操作性
- 根據製造商的需要啟用開箱即用的可互操作設備
.定義ZigBee網絡和堆層模型
- 定義ZigBee設備類型和核心功能
- 使用其接口和服務定義層和模塊
.提供框架以允許分離對ZigBee設備的規範，設計和實現的關注
- 幫助創建和協調在ZigBee中術語的一致使用
.允許未來擴展ZigBee
- 啟用基本ZigBee平台的擴展以及ZigBee應用程序配置文件

## Slide 68: ZigBee Architecture Objectives
Define the ZigBee network and stack models
  Define ZigBee device types and core functions
  Define layers and modules with their interfaces, and services
Provide the framework to allow a separation of concerns for the specification, design, and implementation of ZigBee devices
  Help to create and coordinate consistent use of terms in ZigBee
Allow future extension of ZigBee
  Enable both extension of the basic ZigBee platform as well as ZigBee application profiles
Source: https://www.nxp.com/files/training_pdf/28081_ZIGBEE_OVERVIEW_WBT.pdf
Notes: .支持ZigBee範圍內的所有目標環境和應用程序：
- 確保設備在使用可用帶寬方面高效
.為無線網絡設備提供平台和實施：
- 易於設計和開發ZigBee設備
- 降低當今建設無線解決方案的成本
.通過定義應用程序配置文件確保互操作性
- 根據製造商的需要啟用開箱即用的可互操作設備
.定義ZigBee網絡和堆層模型
- 定義ZigBee設備類型和核心功能
- 使用其接口和服務定義層和模塊
.提供框架以允許分離對ZigBee設備的規範，設計和實現的關注
- 幫助創建和協調在ZigBee中術語的一致使用
.允許未來擴展ZigBee
- 啟用基本ZigBee平台的擴展以及ZigBee應用程序配置文件

## Slide 69: Wireless Networking Basics
Network scan: the ability of a device to detect active channels within its communications range. This range is often called, in personal area networking, the Personal Operating Space (POS).
Creating/Joining a PAN: the ability to form a network on unused channels within the POS. In the case of ZigBee, the network is a PAN. Joining is the ability to join a network within the POS.
Device discovery: the ability to identify the devices on active channels in the PAN.
Service discovery: the ability to determine what features or services are supported on devices within a network.
Binding: the ability to communicate at the application level with other devices in the network.
Source: https://www.nxp.com/files/training_pdf/28081_ZIGBEE_OVERVIEW_WBT.pdf
Notes: .網絡掃描：設備在其通信範圍內檢測活動信道的能力。 這個範圍通常在個人區域網絡中被稱為個人操作空間（POS）。
.創建/加入PAN：在POS中未使用的通道上形成網絡的能力。 在ZigBee的情況下，網絡是PAN。 加入是指加入POS內的網絡的能力。
.設備發現：識別PAN中活動信道上的設備的能力。
.服務發現：確定網絡中的設備上支持哪些功能或服務的能力。
.綁定：在應用程序級別與網絡中的其他設備通信的能力。

## Slide 70: Device Discovery
Association
Disassociation
Synchronizing
Channel Scan

## Slide 71: Association
If device wait a aResponseWaitTime and no any Association response, then Association failure
Coordinator MAC
Device
MAC
Association request
ACK
aResponseWaitTime
Data
request
ACK
Association response
ACK
Beacon
Append device’s
long address in beacon
Notes: 裝置向協調者發出關聯請求Association request
，而協調者回應關聯請求命令確認訊框 ack，假使裝置收到關聯請求回應命令確認訊框後ack，裝置最多在aResponseWaitTime的時間(因為是競爭模式)
之後會嘗試向協調器要求關聯回應命令Association response
，如果裝置不能從協調器獲得關聯回應命令訊框Association response
，則關聯嘗試失敗。
資料來源http://standards.ieee.org/getieee802/download/802.15.4-2003.pdf (p80)
An unassociated device shall initiate the association procedure by sending an associate request command
(see 7.3.1.1) to the coordinator of an existing PAN. If the association request command is received correctly,
the coordinator shall send an acknowledgment frame, thus confirming receipt.
The acknowledgment to an association request command does not mean that the device has associated. The
coordinator needs time to determine whether the current resources available on the PAN are sufficient to
allow another device to associate. The coordinator shall make this decision within aResponseWaitTime
symbols. If the coordinator finds that the device was previously associated on its PAN, all previously
obtained device-specific information shall be removed. If sufficient resources are available, the coordinator
shall allocate a short address to the device and generate an association response command (see 7.3.1.2)
containing the new address and a status indicating a successful association

## Slide 72: Association
In IEEE 802.15.4, association results are announced in an indirect fashion.
  A coordinator responds to association requests by appending devices’ long addresses in beacon frames
Devices need to send a data request to the coordinator to acquire the association result
After associating to a coordinator, a device will be assigned a 16-bit short address.
Notes: 而協調者回應關聯請求命令在beacon frames 通過devices長位址
關聯到一個協調者後，設備將被分配一個 16位的短位址

## Slide 73: Channel Scan
Before starting or joining a PAN, channels are scanned in order from the lowest channel number to the highest
Four channel scans
  Active scan (FFD)
  Passive scan (FFD & RFD)
  Orphan scan (FFD & RFD)
  Energy detection scan (FFD)
During the channel scan, devices suspend beacon transmissions
All devices shall be capable of performing passive and orphan scans
Notes: 頻道掃描：
在開始建立或者加入一個ＰＡＮ前，會掃描所有的頻道，由小到大掃描．
那些設備需要有哪些掃描的功能
ＦＦＤ 基本上四種都需要，ＲＦＤ因為功能較為簡單只需要其中的兩種功能，這些功能在後面幾張投影片會介紹．
在頻道掃描的時候，裝置會暫停 beacon訊號的傳輸
總結來說devices 不管事FFD或者RFD都一定要有passive 和 orphan scans 功能

## Slide 74: Active & Passive Channel Scan
Active Channel Scan
  An active scan allows an FFD to locate any existing coordinator transmitting beacon frames within its POS(Personal Operating Space)
  This is used by PAN coordinator to select a PAN identifier prior to starting a new PAN, or it could be used by a device prior to association
Passive Channel Scan
  A passive scan allows a device to locate any coordinator transmitting beacon frames within its POS
  Passive channel scan could be used by a device prior to association
Notes: 主動頻道掃描:FFD用主動頻道掃瞄以發現在此區域中是否有已存在之coordinator
PAN coordinator在開始一個PAN時也可以使用主動頻道掃瞄選擇PAN identifier , 且裝置可以以此種方法掃瞄後並要求加入PAN
被動頻道掃瞄:裝置使用被動頻道掃瞄以發現coordinator所傳送之beacon frame
裝置可以以此種方法掃瞄後並要求加入PAN

## Slide 75: ED and Orphan Channel Scan
Energy Detection channel scan
  FFD obtains the peak energy in each requested channel
  A prospective PAN coordinator selects a channel for a new PAN
Orphan channel scan
  Allow a device to attempt to relocate its coordinator following a loss of synchronization
Notes: ED頻道掃瞄:一個新創的PAN coordinator 用以讓所有搜尋頻道的裝置能找到頻道上最高峰之能量
Orphan頻道掃瞄:當裝置發成同步遺失時 , 搜尋所有的頻道來尋找以建立連線之父節點

## Slide 76: Superframe Structure
Optional use
Superframe format is defined by the PAN coordinator
The superframe
  Bounded by network beacons
  Sent by the coordinator
  Divided into 16 equally sized slots
The beacon frame is transmitted in the first slot of each superframe

## Slide 77: Superframe Structure

## Slide 78: Superframe structure
CFP
(Contention-Free Period)
GTS 3
GTS 2
GTS 1
CAP
(Contention-Access Period)
Beacon
Inactive
1
0
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Beacon
Active
Transmitted by PAN coordinator. Contains network information,
frame structure and notification of pending node messages.
Network
beacon
Contention-Access
Access by any node using CSMA-CA
Guaranteed
Time Slot
Reserved for nodes requiring guaranteed bandwidth
(Guaranteed Time Slot)
Notes: 在IEEE 802.15.4的規範中，Superframe的格式是由網路的協調者來定義的。
Superframe的時間長短就是為協調者所發出的Beacon時間間隔(Beacon interval)，一個Superframe可以再細分為活動區間(Active portion)跟閒置區間(Inactive portion)，而活動區間又可以再細分為16個小的相同大小的時槽，並且這16個時槽又可以分為競爭區間(Contention-Access Period；CAP)以及免競爭區間(Contention-Free Period；CFP)，
協調者只在活動區間和個人區域網路中的裝置互相收送資料，而在閒置區間則可以進入省電模式以減少電源消耗。
對於協調者以外的裝置來說，它們在沒有資料要傳送時可以進入省電模式。
Beacon訊框在第一個時槽傳送，Beacon訊框的目的有裝置同步、宣告PAN的存在、通知網路中的其他節點告知有暫存的封包存於網路協調者以及告知superframe的結構。
當任何裝置欲在競爭區間跟協調者溝通必須使用時槽型之CSMA/CA的機制來爭取傳送的機會。
Superframe的結構由Beacon訊框中包含的資訊來決定，Beacon Order(BO)決定Beacon發送的間隔，而Superframe Order(SO)則決定活動區間的長短，SO及BO的值皆為0到14之間的整數，且SO≦BO。
活動區的長度被設定為:
aBaseSuperframeDuration × 2SO symbols
aBaseSuperframeDuration為IEEE 802.15.4預設參數。而一個Superframe的長度為:
aBaseSuperframeDuration × 2BO symbols
當SO=15時，代表不使用superframe的架構。如果裝置有要求要使用固定時槽傳輸資料並且亦通過協調者的同意，在Beacon訊框裡亦會告知裝置他們可以使用的固定時槽。然而如果網路協調者不希望使用Superframe也可以不傳送Beacon訊框，此時網路中的裝置將會使用非時槽型的CSMA/CA機制來爭取傳送機會。

## Slide 79: Superframe structure
GTS 3
GTS 2
GTS 1
Beacon
Inactive
1
0
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Beacon
Active
CFP
CAP
SD=aBaseSuperframeDuration*2SOsymbols
BI=aBaseSuperframeDuration*2BOsymbols
  macBeaconOrder (BO) and macSuperframeOrder (SO)
    macBeaconOrder - The interval at which the coordinator shall transmit its beacon frames (0 ~ 14)
    macSuperframeOrder - The length of the active portion of the superframe, which includes the beacon frame (0 ~ macBeaconOrder)

## Slide 80: Superframe structure
The values of BO and the beacon interval (BI) are related as follows:
BI = 15.36  2BO ms, if 0  BO  14
(aBaseSuperframeDuration=960 symbols=15.36ms)
The values of SO and the superframe duration (SD) are related as follows:
SD = 15.36  2SO ms, if 0  SO  BO  14
Note: If BO =15, the coordinator will not transmit beacon and the value of SO shall be ignored. (non beacon-enable network)
Notes: Superframe會把SD的時間平均分成16個time slots。所以每個time slot多長不一定，要看SD的設定。
所以這裏的0~14跟superframe的16個time slots無關，不要搞混了。BO=15也是跟superframe有16個time slots無關。

## Slide 81: Superframe structure
For channels 11 to 26, the length of a superframe can range from 15.36 msec to 215.7 sec (= 3.5 min).
Each device will be active for 2-(BO-SO) portion of the time, and sleep for 1-2-(BO-SO) portion of the time
Duty Cycle:
BO-SO | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | ≧10
Duty cycle (%) | 100 | 50 | 25 | 12 | 6.25 | 3.125 | 1.56 | 0.78 | 0.39 | 0.195 | < 0.1
Notes: aBaseSuperframeDuration = 960symbols
1symbol=16us
960*16us=15.36ms

## Slide 82: 802.15.4 MAC
Channel Access
  Un-slotted CSMA-CA
  Slotted CSMA-CA

## Slide 83: Channel Access
Non Beacon-enable networks
  No beacon frame
  unslotted CSMA/CA channel access mechanism
Beacon-enable networks
  With beacon frame
  Slotted CSMA/CA channel access mechanism

## Slide 84: Un-slotted CSMA-CA
Coordinator provides a beacon only when requested by a node
A device waits for a random period without carrier sense
  One backoff period = 20 symbols (aUnitBackoffPeriod)
Procedure
  Step 1: random backoff
  Step 2: check channel status (CCA)
      Idle  transmit its data
      Busy  wait for another random period before retry

## Slide 85: Un-slotted CSMA-CA
Perform CCA
Channel idle?
NB=NB+1
BE=min(BE+1,macMaxBE)
NB>
macMaxCSMABackoffs?
Failure
Success
Y
Y
N
N
NB=0
BE=macMinBE
Un-slotted CSMA
Delay for random(2BE-1)
unit backoff peroid

## Slide 86: Slotted CSMA/CA Algorithm
PAN coordinator periodically broadcasts a superframe
  A beacon frame, 15 time slots (CAP and GTS), and an optional inactive period
It is similar to the unslotted CSMA-CA but follows the backoff slot boundary
Every device in the PAN shall be aligned with the superframe slot
Notes: 使用Beacon-enable網路裡之時槽型CSMA/CA機制時，當裝置們收到網路協調者所發出的Beacon後，他們會將退後時槽(backoff slot)對準Beacon發出的時間。
在競爭區間中每當一個裝置有資料訊框要傳送時，它必須先等到下一個時槽的起始邊界，然後等待隨機產生的若干個退後時槽時間，當等待的時間結束後，如果這時候頻道是忙碌的，根據random backoff機制，該裝置必須再次等待另一隨機產生的若干個退後時槽時間；如果這時頻道沒有被使用，則裝置可在下一個退後時槽的起始邊界開始傳送資料訊框。

## Slide 87: Slotted CSMA/CA Algorithm
Each device shall maintain three variables
    NB (no. of backoff – retry count) (4)
    CW (contention window size)
      the number of clear slots that must be seen after each backoff
      Initialization: CW=2 and count down to 0 if the channel is sensed to be clear
    BE (backoff exponent)
      BE is related to how many backoff periods a device shall wait before attempting to assess a channel
      macMinBE : 0~3 (default: 3)
      aMaxBE : 5
Notes: 使用Beacon-enable網路裡之時槽型CSMA/CA機制時，當裝置們收到網路協調者所發出的Beacon後，他們會將退後時槽(backoff slot)對準Beacon發出的時間。
在競爭區間中每當一個裝置有資料訊框要傳送時，它必須先等到下一個時槽的起始邊界，然後等待隨機產生的若干個退後時槽時間，當等待的時間結束後，如果這時候頻道是忙碌的，根據random backoff機制，該裝置必須再次等待另一隨機產生的若干個退後時槽時間；如果這時頻道沒有被使用，則裝置可在下一個退後時槽的起始邊界開始傳送資料訊框。

## Slide 88: Slotted CSMA/CA Random backoff
BE：the backoff exponent which is related to how many backoff periods
NB︰number of backoff (periods)
Channel busy → NB=NB+1，BE=min(BE+1,aMaxBE)
BC (Backoff Counter) = random(2BE-1) periods
Beacon
Inactive
1
0
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Beacon
BC=1
CW=1
CW=0
NB=0
BC=3
NB=1
BE=BE+1CW=2
if NB >macMaxCSMABackoffs then failure
Notes: 此為CSMA/CA演算法每個設備在每次嘗試傳輸時都需要維護的三個變數︰NB、CW和BE。
變數NB是嘗試當前訊框(Frame)發送過程中CSMA/CA演算法執行random backoff的次數，在每個新的傳輸嘗試之前NB應初始化為0。
變數BE是backoff 指數，設備試圖評估通道前backoff的時間與BE有關。
變數CW是Contention Window的長度，它表示允許發送前要求通道連續空閒的時間，每次發送嘗試之前CW初始化為2，並且每次探測到通道忙碌時也重定為2，變數CW只用於CSMA/CA演算法。
在時槽式的CSMA/CA演算法中，
MAC層首先（1）初始化變數NB、CW和BE，
然後（2）對準下一個backoff period的邊界，
（3）MAC層隨機延遲隨機個完整backoff period 後，
（4）請求物理層執行通道評估(CCA)，backoof period 亂數的取值範圍是0～ 2BE-1。
在時槽式CSMA/CA演算法中，CCA在backoof period 的邊界處開始執行，而在非時槽式的CSMA/CA演算法中，CCA立即開始執行。
如果通道評估為忙碌，則變數NB和BE都加1。
在時槽式的CSMA/CA演算法中還要把變數CW設為2，如果變數NB的值小於或等於屬性 macMaxCSMABackoffs 的值，則演算法跳轉到（3）隨機延遲隨機個完整backoff period 之步驟重新執行，如果變數NB的值大於屬性 macMaxCSMABackoffs 的值，則CSMA/CA演算法結束，通道存取失敗。
在本圖中，以第一個時槽為第0個時槽來說，STA2在第2個時槽欲存取頻道，執行時槽式的CSMA/CA演算法（1）初始化變數NB、CW和BE，（2）對準下一個backoff period的邊界（3）MAC層隨機延遲隨機個完整backoff period，得到的BC值為1，也就是在1個時槽後會執行（4）物理層執行通道評估(CCA)，如果通道評估的結果為閒置，在時槽式CSMA/CA演算法中MAC層要確保在Contention Window （P.60）之後才開始傳輸資料訊框(Frame)。
為了達到這目的，演算法把CW減1並判斷是否為0，如果CW不為0，則演算法跳轉到（4）請求物理層執行通道評估(CCA)之步驟重新執行，如果CW等於0，則MAC層在下一個backoff period 的邊界處開始發送資料訊框(Data frame)。
如果在非時槽式的CSMA/CA演算法中通道評估為閒置，則MAC層將立即開始發送資料訊框(Data frame)。
而當第4個時槽時，STA1欲存取頻道，執行時槽式的CSMA/CA演算法（1）初始化變數NB、CW和BE，（2）對準下一個backoff period的邊界（3）MAC層隨機延遲隨機個完整backoff period，得到的BC值為3，代表在3個時槽後會執行（4）物理層執行通道評估(CCA)，但這時STA2正在存取頻道，故通道評估(CCA)的結果為忙碌，則變數NB和BE都加1。並保證BE不超過常量aMaxBE。

## Slide 89: Slotted CSMA/CA Random backoff
CW： the number of backoff slots that needs to be clear of channel activity before transmission can commence.
Channel idle → CW=CW-1
CW = 0 → transmission
Beacon
Inactive
1
0
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Beacon
CW=1
CW=0
BC=1
LIFS
BC=5
CW=0
CW=1
Notes: 如果通道評估的結果為閒置，在時槽式CSMA/CA演算法中MAC層要確保在Contention Window 之後才開始傳輸資料訊框(Frame)。
為了達到這目的，演算法把CW減1並判斷是否為0，如果CW不為0，則演算法跳轉到（4）請求物理層執行通道評估(CCA)之步驟重新執行，如果CW等於0，則MAC層在下一個backoff period 的邊界處開始發送資料訊框(Data frame)。
如果在非時槽式的CSMA/CA演算法中通道評估為閒置，則MAC層將立即開始發送資料訊框(Data frame)。
IFS:MAC層需要時間處理來處理物理層的資料，所以訊框後面應預留一段空閒時間，IFS的長度與訊框的大小有關，訊框長度不超過aMaxIFSFrameSize時，使用短的IFS(SIFS)，如果訊框長度大於aMaxIFSFrameSize時，使用長的IFS(LIFS)。

## Slide 90: Slotted CSMA/CA Algorithm
NB=0,CW=2
CSMA-CA
BE=macMinBE
Locate backoff
Peroid boundary
Delay for random(2BE-1) unit backoff peroid
Perform CCA on
backoff period boundary
Channel idle?
CW=2,NB=NB+1
BE=min(BE+1,macMaxBE)
NB>
macMaxCSMABackoffs?
CW=CW - 1
CW=0?
Failure
Success
Y
Y
Y
N
N
N

## Slide 91: Zigbee Networking Assumptions
Devices are pre-programmed for their network function:
  Coordinator scans to find an unused channel to start a network.
  Router (mesh device within a network) scans to find an active channel to join, then permits other devices to join.
  End device will always try to join an existing network.
Devices discover other devices in the network providing complementary services:
  Service discovery can be initiated from any device within the network or performed via Gateways from devices outside the network
Devices can be bound to other devices offering complementary services:
  Binding provides a command and control feature for specially identified sets of devices.
Source: https://www.nxp.com/files/training_pdf/28081_ZIGBEE_OVERVIEW_WBT.pdf
Notes: .設備針對其網絡功能進行了預先編程：
-協調器掃描以找到未使用的通道來啟動網絡。
-路由器（網絡中的網格設備）掃描以找到要加入的可用頻道，然後允許其他設備加入。
-終端設備將始終嘗試加入現有網絡。
.設備發現網絡中的其他設備提供補充服務：
-服務發現可以從網絡內的任何設備發起或通過網絡從網絡外的設備執行
.設備可以綁定到提供補充服務的其他設備：
-綁定為特定標識的設備提供命令和控制功能。

## Slide 92: Zigbee Routing Architecture
Star Network - one coordinator networked with one or more end devices
Cluster Tree - where devices branch off of a tree, the network backbone.
Mesh network - Routing paths are not as constrained as in the cluster tree topology.
Mesh networking permits path formation from any source to any destination device.
Source: https://www.nxp.com/files/training_pdf/28081_ZIGBEE_OVERVIEW_WBT.pdf
Notes: 星形網絡 - 一個協調器與一個或多個終端設備聯網
集群樹狀 - 設備從樹上分支，網絡骨幹。
網絡網絡 - 路由路徑不受集群樹拓撲中的約束。網狀網絡允許從任何源到任何目的地設備的路徑形成。

## Slide 93: Concept of Routing for Tree Topology

## Slide 94: Routing for Tree topology
In a tree networks, when a device receives a packet, it first checks if it is the destination or one of its child end devices is the destination
  If so, accept the packet or forward it to a child
  Otherwise, relay it along the tree
  This is made possible by its addressing scheme!!
Notes: 在一個樹狀網路中，ZigBee協調者和路由器延著樹狀結構傳遞封包。
當一個裝置 n 接收到封包，首先會檢查他是否是目的地的節點或者他的一個小孩是否為目的地?
如果是，則裝置n將接受該封包或是將該封包傳送給指定小孩。
否則，它將沿著樹轉送封包給它的小孩或是給它的父節點。

## Slide 95: Device Addressing
95
Two or more devices communicate on the same physical channel constitute a WPAN.
  A WPAN includes at least one FFD (PAN coordinator)
  Each independent PAN will select a unique PAN identifier
Each device operating on a network has a unique 64-bit extended address. This address can be used for direct communication in the PAN.
A device also has a 16-bit short address, which is allocated by the PAN coordinator when the device associates with its coordinator.

## Slide 96: ZigBee Network Address Format
Starts out with a unique 64-bit IEEE address
  64 bits (8 bytes)
  Organizational Unique Identifier (OUI):24 bits
  Original Equipment Manufacturer (OEM):40 bits
Joining the network, each node is assigned a unique (within that network) 16-bit short address.
Notes: ZigBee的網路位置長度。
再加入網路時，每個節點會
另外分配長度為16bits的位置。

## Slide 97: Address Assignment Algorithm
Network addresses are assigned to devices with a distributed address assignment scheme in ZigBee.
Three network parameters are determined by ZigBee coordinator.
  A ZigBee router has the maximum number of children (Cm) .
  A parent node has the maximum number of child routers (Rm).
  The depth of the network is (Lm).
A parent device utilizes Rm, Cm ,and Lm to compute a parameter called Cskip
  It is used to compute the size of its children’s address pools
Notes: ZigBee 網路層的協定中規範了分散式網路位置分配的演算法，此演算法
用來分配網路位置給加入該網路的裝置。
當網路行成時，ZigBee coordinator 會先定義一個路由器最多可以容許連
線的裝置各數(即Cm)和最多的子ZigBee router的數量(Rm)和網路的深度Lm。

## Slide 98: Address Assignment Algorithm
ZigBee provides rules that Cm >= Rm, therefore ZigBee router can provide at least (Cm-Rm) ZigBee connections of ZigBee devices.
The address of device is assigned by parent router. For ZigBee coordinator, the whole network is divided into (Rm+1) blocks.
Rm blocks will be allocated to its Rm sub-router, and the final block is preserved for the (Cm-Rm) end devices connected with it.
ZigBee router(in depth d) uses these parameters to compute a Cskip value. (The depth of coordinator is defined as 0 )
Notes: 算出每一層網路深度的Cskip 函數。
Cskip是指parent的一個subtree最大的node數
ZigBee 規定 Cm>=Rm，所以一個ZigBee的路由器
至少可以提供(Cm-Rm)個終端設備連結上它。

## Slide 99: Address Assignment Algorithm
If a parent node at depth d has an address Aparent,
  the nth child router is assigned to address Aparent+(n-1)×Cskip(d)+1
  nth child end device is assigned to address Aparent+Rm×Cskip(d)+n
以A為例，A是C的第2個child;
A的位址是0+(2-1)*31+1=32
C的Cskip=(6-4-6*4^2+1)/(1-4)=31
(Cm=6, Rm=4, Lm=3)
  Aparent+Rm×Cskip(d)+n
Aparent+(n-1)×Cskip(d)+1
Notes: 舉例來說，A點的位址 是 0 + (2-1) * 31 + 1 = 32，0是parent node (C)的位址，2是指C第幾個子孫，31是指C的Cskip=(6-4-6*4^2+1)/(1-4)=31
上面那個點的位址則是 0 + 4 * 31 + 1 = 125，0是指parent node (C)的位址，4的是C的Rm數，31是指C的Cskip，1是指C第幾個子孫

## Slide 100: Routing for Tree topology
When device n receive a packet, device will check whether the address of packet destination is same as itself address or it’s descendants address or not
    If yes ; An<Adest<An+ Cskip(d-1)
      Receive it or pass to it’s descendants
    If No
      Pass this packet to it’s parent node
以A為例: range(32<..<32+31)
Notes: 在一個樹狀網路中，ZigBee協調者和路由器延著樹狀結構傳遞封包。
當一個裝置 n 接收到封包，首先會檢查他是否是目的地的節點或者他的一個小孩是否為目的地?
如果是，則裝置n將接受該封包或是將該封包傳送給指定小孩。
否則，它將沿著樹轉送封包給它的小孩或是給它的父節點。

## Slide 101: Routing for Tree topology
The forwarding address will be
Example:
  Src:38  Dst:45
  Src:38  Dst:92
在A時，A=33+「(45-33)/7」*7=40
在A時，forward to parent node
Notes: 假設 n的位置是 An 且深度是 d， n將此一封包轉送給其他小孩 (假設此封包目的地是Adest)
則以下條件會滿足 =>
An < Adest < An+Cskip + (d-1) 且此封包會轉送給位置為 => Ar = A+1+{ [Adest-(A+1)]/Cskip(d)}(取下界) * Cskip(d)
的小孩 。如果目的地位置 Adest並非裝置n的 後代，則n將該封包轉送給其父節點

## Slide 102: Application Support Features
Profile: Profiles are used to define a device’s application capability and drive the application details. An example of a profile would be Home Control—Lighting.
Endpoint: Endpoints are the physical dimensions added to a ZigBee device which permit multiple application support, addressed by the Endpoint number (0-31).
Interface: Interfaces are defined per endpoint and allow such things as extra proprietary capability extensions and backward compatibility.
Key Relationships:
  Maximum of 30 Endpoints per ZigBee device (0 is reserved to describe the device itself and 31 is reserved for broadcast messaging to all endpoints)
  Maximum of 8 Interfaces per Endpoint
  One Profile described per Interface
Source: https://www.nxp.com/files/training_pdf/28081_ZIGBEE_OVERVIEW_WBT.pdf
Notes: .配置文件：配置文件用於定義設備的應用程序功能並驅動應用程序詳細信息。 配置文件的示例將是家庭控制燈光。
.端點：端點是添加到ZigBee設備的實體尺寸，允許多個應用程序支持，由端點號（0-31）尋址。
.接口：每個端點定義接口，並允許額外的專有能力擴展和向後兼容性。
.關鍵關係：
>每個ZigBee設備最多30個端點（0用於描述設備本身，31用於廣播消息到所有端點）
>每個端點最多8個接口
>每個接口描述一個配置文件

## Slide 103: IEEE 802.15.4e
2008: TSMP is standardized in ISA100.11a
  The IEEE 802.15.4e Working group is created.
  Issue: IEEE 802.15.4-2006 MAC is ill-suited for low-power multi-hop network because of
    high energy consumption due to relay/router nodes
    use of a single channel that implies interference and multi-path fading
  Final aim: to redesign the existing IEEE 802.15.4-2006 MAC Std. and make it suitable for low-power multi-hop networks in industrial applications

## Slide 104: IEEE 802.15.4e
2009: TSMP is standardized in WirelessHART
2010: Part of IEEE 802.15.4e draft
2011: IEEE802.15.4e draft in Sponsor Ballot (opened on 27 July 2011 and closed on 28 August with 96% of votes being affirmative)
16 April 2012: IEEE802.15.4e TSCH published

## Slide 105: IEEE 802.15.4e
Enhancements over IEEE 802.15.4
  Low Energy
  Information Elements
    extensible mechanism to exchange information at the MAC sublayer
  Multipurpose Frame
    can address a number of MAC operations
  MAC Performance Metric
    Provide upper layer feedback on the channel quality
  Fast Association

## Slide 106: IEEE 802.15.4e
MAC operation modes
  Time Slotted Channel Hopping (TSCH)
  Deterministic and Synchronous Multi-channel Extension (DSME)
  Low Latency Deterministic Network (LLDN)

## Slide 107: IEEE 802.15.4e

## Slide 108: MAC Operation Modes

## Slide 109: MAC Operation Modes

## Slide 110: IEEE 802.15.4e TSCH
Based on IEEE802.15.4-2006 PHY (to profit from embedded PHYs)
TSCH: TimeSlotted (Synchronized), to allow for distributed implementation
TSCH: Channel Hopping, to give resilience to interference/multi-path fading

## Slide 111: TSCH: TimeSlotted

## Slide 112: Time Slot

## Slide 114: TSCH Schedule
Each node follows a communication schedule
A schedule is a matrix of cells, each of them indexed by a slotOffset and a channelOffset
Each cell can be assigned to a pair of nodes, in a given direction
A scheduled cell can be used by one and/or multiple couples of devices (i.e., dedicated and/or shared)

## Slide 115: TSCH Schedule
A schedule is built according to the specific requirements of the application
  Trade-off between energy consumption, robustness and latency
Different approaches for building a schedule:
  Centralized (e.g., PCE-based)
  - PCE responsible for building and maintaining the schedule
  - Efficient for static networks
  Distributed (e.g., MPLS-like)
  - Nodes decide locally which cells they will use for
  communicating with their neighbors
  - Suitable for mobile networks with many gateways
  - Scalable with large network size

## Slide 116: TSCH Channel Hopping
Absolute Slot Number

## Slide 118: IPv6 over TSCH

## Slide 119: 802.15.4 Protocol Stacks

## Slide 120: 802.15.4g
Wireless Neighborhood Area Network (WNAN)
IPv6 based Wireless Smart Utility Network (Wi-SUN) based on IEEE 802.15.4g
  IEEE 802.15.4g, also known as the Smart Utility Networks (SUN), was approved by IEEE in March, 2012
Initially Japan focused, now expanding globally (US, South East Asia, India, Europe)
Target smart utility use cases
MAC may be based on or not based on 802.15.4

## Slide 121: 802.15.4g
Frequency:
  868 MHz (EU), 915 MHz (USA), 2.4 GHz ISM bands (worldwide)
Maximum bandwidth: 200kHz~1.2MHz
Data rate: 50kbps ~ 1Mbps
Modulation: FSK, OFDM, OQPSK
Range: 100m
Application: FAN, HAN, smart utility networks, smart grid, smart metering

## Slide 122: 802.15.4g
3 physical layer (PHY) standards supported:
  MR-FSK*: 2FSK and 4FSK modulation used
  MR-OFDM: 4 options with different FFT size and bandwidths
  MR-O-QPSK*: DSSS and multiplexed DSSS used
Frequency bands depend on regulatory requirements, may include bands around 169, 450-510, 780, 863-870, 896-960, 1427-1518, and 2400-2483 MHz
Wi-SUN Alliance PHY conformance tests and profiles being developed for MR-FSK PHY.

## Slide 123: 802.15.4g

## Slide 124: Bluetooth Low Energy

## Slide 125: Bluetooth Low Energy (BLE)
Bluetooth is a wireless technology standard for building personal area networks (PANs).
It is based on short-wavelength UHF radio waves in the ISM band from 2.4 to 2.485 GHz for fixed and mobile devices.
Invented by telecom vendor Ericsson in 1994, it was originally conceived as a wireless alternative to RS-232 data cables.
Bluetooth Low Energy (BLE) is a light-weight subset of classic Bluetooth and was introduced as part of the Bluetooth 4.0 core specification.
While there is some overlap with classic Bluetooth, BLE actually has a completely different lineage and was started by Nokia as an in-house project called 'Wibree' before being adopted by the Bluetooth SIG.
Notes: . 藍牙是用於建立個人局域網（PAN）的無線技術標準。
. 它基於固定和移動設備的2.4到2.485 GHz的ISM頻帶中的短波長UHF無線電波。
. 它由電信供應商愛立信於1994年發明，最初被認為是RS-232數據電纜的無線替代品。
. 藍牙低功耗（BLE）是經典藍牙的一個輕重量子集，是藍牙4.0核心規範的一部分。
. 雖然與藍牙有一些重疊，但BLE實際上具有完全不同的系統，並由諾Nokia在被藍牙SIG採用之前作為一個名為“Wibree”的內部項目啟動。

## Slide 126: Protocol Stack

## Slide 127: Generic Access Profile (GAP)
GAP governs connections and advertising in Bluetooth.
GAP defines various roles for devices, but the two key concepts to keep in mind are Central Devices and Peripheral Devices.
  Peripheral devices are small, low power, resource constrained devices that can connect to a much more powerful central device. Peripheral devices are things like a heart rate monitor, a BLE enabled proximity tag, etc.
  Central devices are usually the mobile phone or tablet that you connect to with far more processing power and memory.
Notes: 通用訪問配置文件（GAP）
. GAP控制藍牙中的連接和廣告。
. GAP定義了設備的各種角色，但有兩個關鍵概念很重要：中央設備和外圍設備。
- 外圍設備是小型，低功率，資源受限的設備，可以連接到更強大的中央設備。 外圍設備就像心率監視器，BLE的接近標籤等。
- 中央設備通常是您連接到的移動電話或平板電腦，具有更多的處理能力和記憶儲存。

## Slide 128: Advertising and Scan Response Data
Two ways to send advertising out with GAP. Both payloads are identical and can contain up to 31 bytes of data.
The Advertising Data payload (mandatory): that is constantly transmitted out from the device to let central devices in range know that it exists.
The Scan Response payload (optional): that central devices can request, and allows more information fit in the advertising payload such as strings for a device name, etc.
Notes: .使用GAP發送廣告的兩種方式。 兩個內容(payloads)是相同的，並且可以包含多達31個字節的資訊。
.廣告數據有效內容（強制性）：不斷地從設備發出，以使範圍內的中央設備知道它存在。
.掃描響應有效內容（可選）：中央設備可以請求，並允許更多信息適合廣告有效內容，例如設備名稱的字符串等。

## Slide 129: Advertising Process
A peripheral will set a specific advertising interval, and every time this interval passes, it will
retransmit it's main advertising packet. If a listening device is interested in the scan response
payload (and it is available on the peripheral) it can optionally request the scan response
payload, and the peripheral will respond with the additional data.
Source: https://learn.adafruit.com/introduction-to-bluetooth-low-energy/introduction
Notes: 外設將設置特定的廣告時間間隔，並且每次這個時間間隔通過，它都會重傳它的主要廣告包。
如果聽音裝置對掃描回應了感興趣的內容（並且它在外圍設備上可用），它可以可選地請求掃描回應有效內容，並且外圍設備將用附加數據進行回應。

## Slide 130: Advertising via Broadcast
By including a small amount of custom data in the 31 byte advertising or scan response payloads, you can use a low cost Bluetooth Low Energy peripheral to sent data one-way to any devices in listening range, as shown in the illustration below. This is known as Broadcasting in Bluetooth Low Energy.
https://learn.adafruit.com/introduction-to-bluetooth-low-energy/introduction
Notes: This is the approach use by Apple's iBeacon, for example, which inserts a custom payload in the main advertising packet, using the Manufacturer Specific Data field.
一旦你在外圍設備和中央設備之間建立連接，廣告進程通常會停止，您通常將無法再發送廣播數據包，
並且您將使用GATT服務和特性在雙向進行通信。

## Slide 131: GATT
Once a connection between a peripheral and a central device is established, the advertising process will stop
  No advertising packets will be sent out
Use GATT services and characteristics to communicate in both directions
Notes: 一旦你在外圍設備和中央設備之間建立連接，廣告進程通常會停止，您通常將無法再發送廣播數據包，
並且您將使用GATT服務和特性在雙向進行通信。

## Slide 132: Exclusive Connection of GATT
With GATT, connections are exclusive
  A BLE peripheral can only be connected to one central device (a mobile phone, etc.) at a time!
  As soon as a peripheral connects to a central device, it will stop advertising itself and other devices will no longer be able to see it or connect to it until the existing connection is broken.
Notes: 使用GATT，連接是獨占的。 即BLE外設只能一次連接到一個中央設備（手機等）。
一旦外圍設備連接到中央設備，它將停止廣播自己(advertise)，並且其它設備將不再能夠看到它或連接到它，直到現有連接斷開。

## Slide 133: Connected Topology
A peripheral can only connect to a central device but a central device can connect up
To 7 peripherals. Once a connection is established between a peripheral and a central
device, communication can take place in both directions.
https://learn.adafruit.com/introduction-to-bluetooth-low-energy/introduction
Notes: 外設只能連接到中央設備，但中央設備可以連接到7個外設。
一旦在外圍設備和中央設備之間建立連接設備，通信可以在兩個方向上發生。

## Slide 134: Server-Client in GATT Transactions
Client: Typically sends a request to the GATT server. The client can read and/or write attributes found in the server.
Server: One of the main roles of the server is to store attributes. Once the client makes a request, the server must make the attributes available.
The IoT device is known as the GATT Server, which holds the ATT lookup data and service and characteristic definitions, and the GATT Client (smart phone/tablet) sends requests to this server.
Notes: .客戶端：通常向GATT服務器發送請求。 客戶端可以讀取和/或寫入在服務器中找到的屬性。
.伺服器：伺服器的主要角色之一是存儲屬性。 一旦客戶端發出請求，伺服器必須使屬性可用。
.物聯網設備稱為GATT服務器，它保存ATT查找數據和服務和特性定義，GATT客戶端（智能手機/平板電腦）向此伺服器發送請求。

## Slide 135: GATT Transactions
All transactions are started by the master device, the GATT Client, which receives response from the slave device, the GATT Server.
When establishing a connection, the peripheral will suggest a 'Connection Interval' to the central device, and the central device will try to reconnect every connection interval to see if any new data is available, etc.
The following diagram illustrates the data exchange process between a peripheral (the GATT Server) and a central device (the GATT Client), with the master device initiating every transaction:
https://learn.adafruit.com/introduction-to-bluetooth-low-energy/introduction
Notes: . 所有事務由主設備啟動，即GATT客戶端。GATT客戶端從子設備(GATT服務器)接收回應。
. 當建立連接時，外圍設備將向中央設備提出“連接間隔”，並且中央設備將嘗試重連每個連接間隔以查看是否有任何可用的新數據等。
. 下圖說明了外設（GATT服務器）和中央設備（GATT客戶端）之間的數據交換過程，每個事務由主設備啟動：

## Slide 136: GATT Services and Characteristics
GATT is an acronym for the Generic Attribute Profile.
It defines the way that two Bluetooth Low Energy devices transfer data back and forth using concepts called Services and Characteristics.
It makes use of a generic data protocol called the Attribute Protocol (ATT), which is used to store Services, Characteristics and related data in a simple lookup table using 16-bit IDs for each entry in the table.
Notes: . GATT是通用屬性配置文件的縮寫。
. 它定義了兩個藍牙低功耗設備使用稱為服務和特性的概念來回傳輸數據的方式。
. 它使用稱為屬性協議（ATT）的通用數據協議，該協議用於在簡單查表中存儲服務，特性和相關數據，使用表中每個條目的16位元的ID。

## Slide 137: Services and Characteristics
GATT transactions in BLE are based on high-level, nested objects called Profiles, Services and Characteristics.
Profile: This is simply a pre-defined collection of Services compiled by either the Bluetooth SIG or by the peripheral designers.
Service: contains specific chunks of data called characteristics. A service can have one or more characteristics, and each service distinguishes itself from other services by means of a unique numeric ID called a UUID.
Characteristic: encapsulates as single data point. Similarly to Services, each Characteristic has a pre-defined UUID. Used to send data back to the BLE peripheral.
https://learn.adafruit.com/introduction-to-bluetooth-low-energy/introduction
Notes: BLE中的GATT是基於高階、嵌套的物件，為配置文件，服務和特性。
.配置文件：這只是由藍芽SIG或外圍設計師編制的服務的預定義集合。
.服務：包含稱為特性的特定數據塊。 服務可以具有一個或多個特徵，並且每個服務通過稱為UUID的唯一數字ID將自身與其他服務區分開。
.特性：封裝為單個數據點。 與服務類似，每個特性都有一個事先定義的UUID。 用於將數據發送回BLE外設。

## Slide 138: GATT Services

## Slide 139: Blood Pressure Service Characteristics

## Slide 140: A Comparison between ZigBee, BT and BLE
Feature | ZigBee | Bluetooth Classic (BT) | Bluetooth Smart
Design Focus | Wireless networking among sensors | Wireless keyboards, mouse, headsets | Wireless sensor and fitness devices
IEEE Standard | 802.15.4 | 802.15.1 | 802.15.1
Network Type | Mesh, ZigBee PRO | Piconet, Master/Slave; Scatternet | Scatternet
Distance | 75-100m line of sight | 10m (33ft) min | >10m >(33ft)
Nodes Connected, max | 65000 | 8 | N/A
Operating Band | 2.400 Ghz-2.4835 GHz ISM band 16 channels, 5MHz apart, 2MHz used Direct Spread Spectrum | 2.400 Ghz-2.4835 GHz ISM band 79 1-MHz channels Frequency Spread Spectrum | 2.400 Ghz-2.4835 GHz ISM band 40 2-MHz channels Frequency Spread Spectrum
Throughput | 0.03Mbps | 1-3Mbps | 0.27Mbps
Latency with Connect | 15ms | 100ms - 3sec | 3-6ms
Type of Data | Operational instructions Low data rate | Continuous streaming All types of data; text, multimedia Relatively high speeds | Burst
Voice | No | Yes | No
Security | EAP (Extensible Authentication Protocol) | 56/128-bit and application layer user defined | 128-bit AES (Advanced Encryption Standard) with Counter Mode CBC-MAC and application layer user defined
Power Consumed (dependent on application) | 30mW | 100 mW | 0.01-0.5W
Modulation | Direct Sequence Spread Spectrum | Frequency Hopping Spread Spectrum | Gaussian Frequency Shift Keying
Source: http://www.allaboutcircuits.com/technical-articles/zigbee-vs-bluetooth-and-bluetooth-smart/
Notes: ZigBee，藍芽和BLE之間的比較

## Slide 141
Source: http://www.allaboutcircuits.com/technical-articles/zigbee-vs-bluetooth-and-bluetooth-smart/
Notes: ZigBee，藍芽和BLE之間的比較

## Slide 142: Bluetooth 5
Officially unveiled on 16 June 2016
Mainly focused on Internet of Things technology
Features
  Slot Availability Mask (SAM)
  2 Mbit/s PHY for LE
  LE Long Range
  High Duty Cycle Non-Connectable Advertising
  LE Advertising Extensions
  LE Channel Selection Algorithm #2

## Slide 143: Summary
An M2M area network consists of many types of sensors/actuators/devices and (wireless) communication protocols.
We show many examples of those sensors/ actuators/devices.
We cover three examples of M2M area protocols: ANSI C12 Suite, ZigBee (IEEE 802.15.4), Bluetooth Low Energy (BLE).
Sensor platforms such as Arduino and Raspberry Pi are important tools for connecting and enabling sensors/actuators.
Notes: .M2M區域網絡包括許多類型的傳感器/致動器/設備和（無線）通信協定。
.我們展示了許多傳感器/執行器/設備的例子。
.我們涵蓋了M2M區域協議的三個示例：ANSI C12套件，ZigBee（IEEE 802.15.4），低功耗藍芽（BLE）。
.傳感器平台如Arduino和Raspberry Pi是連接和啟用傳感器/執行器的重要工具。

## Slide 144: Appendix

## Slide 145: Example IoT Devices

## Slide 146: Game Drone – Parrot Ar. Drone (1)
http://ardrone.parrot.com/parrot-ar-drone/usa/
With its own generated WiFi network, players can create a game party where others
players can join and play against each other (e.g., AR.FlyingAce)
A quadricopter made in carbon fiber and high resistance PA66 plastic
MEMS (Micro-Electro-Mechanical Systems) and video processing to ensure an intuitive
piloting of a radio controlled object
WiFi and video streaming for a modern interface with an iPhone™ or iPod touch®
Images processing software for augmented reality
One front camera (wide angle), one vertical camera (high speed), one ultrasound altimeter
Notes: 遊戲無人機 - Parrot Ar. Drone ( 1 )
‧http://ardrone.parrot.com/parrot-ar-drone/usa/
‧藉由其自身產生的WiFi網路，玩家可以創建一個遊戲派對，讓其他玩家可以加入和相互對戰（例如，AR.FlyingAce）。
‧一個由碳纖維和高電阻PA66塑料所製成的四螺旋槳直昇機。
‧透過MEMS（微機電系統）和視訊處理，以確保可以直覺式的駕駛此無線電控制物件
‧在iPhone™或iPod touch®上具WiFi和視訊流的現代化介面
‧擴增實境的影像處理軟體 ‧一個前置相機（廣角），一個垂直相機（高速），一個超音波測高儀

## Slide 147: Game Drone – Parrot Ar. Drone (2)
*** Embedded Computer System
ARM9 468 MHz processor
DDR 128 Mbyte at 200MHz
WiFi – 802.11 b/g
USB high speed
Linux OS
*** Development tool
Download-able Software Development Kit to develop innovative video games
Open Game API enabling projects changing the way video games are played, both indoor and outdoor
Notes: 遊戲無人機 - Parrot Ar. Drone ( 2 )
‧嵌入式電腦系統
–ARM9 468 MHz 處理器
–DDR 128 Mbyte at 200MHz
–WiFi – 802.11 b/g
–USB 高速
–Linux OS
‧開發工具 –可下載的軟體開發工具包，用來開發創新性電視遊戲 –開放的遊戲API使專案可以改變電視遊戲的玩法，不論在室內還是室外

## Slide 148: Surveillance Robot – WowWee Rovio (1)
http://www.wowwee.com/en/products/tech/telepresence/rovio
Wi-Fi enabled mobile robot with webcam that lets you view and interact with its environment through streaming video and audio, wherever you are, via a browser with IP connection
Free iPhone and Android APP enables to move your Rovio by simply tiling the smartphone in the direction you want to travel.
requires some setting adjustment or firmware update to get good video quality or play back paths accurately, or docking in time
Notes: 監視機器人– WowWee Rovio ( 1 )
‧http://www.wowwee.com/en/products/tech/telepresence/rovio
‧具Wi-Fi功能以及網路相機的移動機器人，讓您不論身在何處，只要透過具IP連線的瀏覽器來接收視訊流和聲音，就可以觀看機器人所處環境並與環境互動。
‧免費的iPhone和Android應用程式，透過在智慧型手機螢幕上觸碰您要的方向，就可以操控您的Rovio往指定方向移動。
‧需要透過調整設定或更新韌體，來獲得良好的視訊品質，或是準確地重播路徑，或是及時返回底座

## Slide 149: Surveillance Robot – WowWee Rovio (2)
Detect the computer setting and guides the user through the setup process
Its head-mounted, moveable VGA camera and wide range of vision enable you to see and hear (via 1 x Speaker and 1 x microphone for 2-way audio) exactly what Rovio sees and hears, on your screen, anywhere.
Set waypoints so that Rovio can navigate itself (with 3 x Omni-directional wheels) around your home, without having to control each step yourself
At the click of a button, send Rovio back to the charging dock (with built-in TrueTrack Beacon** ) using its self-docking capabilities - even when you are not at home
Guide Rovio through dimly lit locations with the aid of its built-in LED headlight.
USB connectivity
Rechargeable NiMH battery
** Rovio requires additional TrueTrack Room Beacons to navigate or self-dock across multiple rooms.
Notes: 監視機器人– WowWee Rovio ( 2 )
‧檢測電腦的設置並引導用戶完成安裝 ‧裝在它頭上的可移動VGA相機和廣泛的視野，使您能夠在任何地方，都可以透過螢幕，完整地看到和聽到Rovio的所見所聞 ( 經由一個揚聲器和一個麥克風
及二路音頻)
‧設置路線點，則Rovio可以自行在您的家中移動（經由三個全向車輪），而無需由您來控制每個步驟
‧點擊一個按鈕後，Rovio會自行返回充電底座( 藉由內建的TrueTrack Beacon ) - 即使您不在家
‧借助其內建的LED頭燈，Rovio能通過昏暗的地方
‧USB連接功能 ‧鎳氫充電電池 ‧Rovio需要額外加裝TrueTrack Room Beacons，才能自行移動通過數個房間或是返回底座

## Slide 150: Smart Meter – Elster A3 ALPHA SmartMeter (1)
Notes: 智慧電表–Elster A3 ALPHA SmartMeter ( 1 )
‧SmartSynch’s C&I 儀表解決方案的特色是通訊模組，而Elster A3 ALPHA電表便是和此模組作結合
‧http://www.smartsynch.com/SmartSynch_elster_a3.htm
‧此解決方案提供可啟動智能( 關鍵用量與資料傳輸速率 ) 在安全公用GSM/GPRS無線網路與網際網路上–取代繁瑣的、昂貴的專用網路

## Slide 151: Smart Meter – Elster A3 ALPHA SmartMeter (2)
Features a host of key monitoring and communication functionalities, including
Flexible Two-Way Data Retrieval
Scheduled and On-Demand Reads
Automated Interval Read Retrieval
Real-Time Interval Reads
Automated Register, Self-Read and TOU (Total Ozone Unit) Retrieval
Instrumentation Profiling
Current and Voltage Profiling
Critical Peak Pricing
Demand Resets
Real-Time Meter Event and Alarm Retrieval
Notes: 智慧電表–Elster A3 ALPHA SmartMeter ( 2 )
‧具有多個與關鍵監控和通訊功能有關的特色，包括：
  –彈性的雙向數據檢索 –可預定和依需求讀取
  –自動間隔讀取檢索 –即時間隔讀取 –自動註冊，自行讀取和TOU檢索 –儀表剖析 –電流和電壓分析 –關鍵高峰定價 –需求重置 –即時儀表事件和報警檢索

## Slide 152: Smart Meter – Elster A3 ALPHA SmartMeter (3)
Real-Time Power Outage and Power Restoration Alarms
Power Quality Monitoring and Alarms
Demand Threshold Monitoring and Alarms
Service Diagnostics and Tamper Detection
Meter Clock Synchronization
SmartMeter Status Display
Automated Meter Registration
Secure and Encrypted Data Transmissions
Supports Reads from Itron MV-90 Software
Supports Reads from Elster MAS Software
Remote Meter Programming
Over-The-Air SmartMeter Module Firmware Upgrade
Notes: 智慧電表–Elster A3 ALPHA SmartMeter ( 3 )
‧即時停電和恢復供電警報
‧電力品質監測和警報 ‧需求門檻監測和警報 ‧服務診斷和篡改偵測 ‧電表時鐘同步 ‧智慧電表狀態顯示 ‧自動化電表註冊 ‧安全和加密的數據傳輸 ‧支援讀取Itron MV-90軟體 ‧支援讀取Elster MAS軟體 ‧遠程電表編程 ‧空中下載智慧電表模組韌體升級檔

## Slide 153: Cleaning Robot with IP Camera – Ankaka G182 (1)
Robot vacuum cleaner
WiFi IP camera
Virtual wall and charging station
Proprietary software
http://www.ankaka.com/intelligent-robot-vacuum-cleaner-with-wireless-ip-camera-wifi-ip-camera_p1165.html
Notes: 具IP相機的清潔機器人–Ankaka G182 ( 1 )
‧機器人真空吸塵器 ‧WiFi IP相機 ‧虛擬牆和充電站 ‧專用軟體
‧http://www.ankaka.com/intelligent-robot-vacuum-cleaner-with-wireless-ip-camera-wifi-ip-camera_p1165.html

## Slide 154: Cleaning Robot with IP Camera – Ankaka G182 (2)
Applications include: - DVS application (Designed to identify IP addresses and Modify IP Addresses) - IP Camera Center (View, record, control, and access multiple functions and features of the robot vacuum cleaner with the WiFi IP camera) - IP Camera Player - Plays back recorded video footage
Program it to clean while away from home
Auto Charging station, meaning it will recharge when it is low on power automatically
Use the virtual wall unit to prevent the robot vacuum cleaner from venturing into areas you do not wish it to go
As with all vacuum cleaners, the robot vacuum cleaner does not empty itself, so you will need to clean out the units dust bin after every cleaning cycle
For best results it is recommend that you observe the robot vacuum cleaner operate in each room of your house the first time so you can make sure the room layout and furnishings do not interfere with the units navigation
Notes: 具IP相機的清潔機器人–Ankaka G182 ( 2 )
‧應用程式包括：
  –DVS應用程式（設計來識別IP位址和修改IP位址）
  –IP相機中心（查看，記錄，控制和使用具WiFi IP相機的機器人真空吸塵器其多種功能和特性 )
  –IP相機播放器 - 播放錄製的視訊片段
‧可以在機器人上編程，在您不在家時，它會自動清潔
‧自動充電站，這表示當機器人快沒電時，它會自行去充電
‧使用虛擬牆裝置，以防止機器人真空吸塵器涉足您不希望它去的領域 ‧就像一般的真空吸塵器，機器人真空吸塵器也沒辦法自己清理集塵袋，所以在每次機器人作完清潔後，您都要替它清理集塵袋
‧為了達到最佳效果，建議當機器人真空吸塵器在您房子中的每個房間作第一次清潔時，您也在一旁觀察它，以確保房間的佈局和陳設不會干擾機器人的移動

## Slide 155: Cleaning Robot with IP Camera – Ankaka G182 (3)
Moulded ABS body, pressure sensitive front bumper, two castor style front wheels, large traction grip rear wheels
Height From Floor: 1 inch (approx 2.5cm)
Movement: 360 degrees
Working Time Per Charge: 70 Minutes
Usual Charging Time: 3.5 hours
Noise Level:<50db
Notes: 具IP相機的清潔機器人–Ankaka G182 ( 3 )
‧模組式ABS機身，壓力敏感的前置緩衝器，二個萬向輪風格的前輪，大型牽引後輪 ‧離地高度：1英寸（約2.5公分） ‧可移動角度：360度 ‧每次充電後可使用時間：70分鐘 ‧通常充電所需時間：3.5小時 ‧噪音值：<50分貝

## Slide 156: iRobot Create (1)
Create is preassembled and ready to use right out of the box.
Beginners can observe the robot's behavior in any of the 10 demonstration modes or program the robot by downloading scripts with any basic terminal program.
Advanced users can write custom software using a variety of methods that take advantage of the robot's "streaming sensor data" mode for more control of the robot.
Highly advanced users can write programs for completely autonomous operations.
Create accessories include a Bluetooth Access Module (BAM) for wireless communication
http://store.irobot.com/shop/index.jsp?categoryId=3311368
Notes: iRobot Create ( 1 )
‧Create預先已作好設置，當您開箱後即可馬上使用 ‧初學者可以觀察此機器人具有的十個示範模式下的各種行為，或是經由任意基本終端程式去下載腳本來替機器人作編程
‧進階用戶可以使用各種能發揮機器人“串流感測數據”模式的方法來編寫自定義的軟體，以便對機器人作更多控制
‧熟練用戶可以替機器人編寫完全自主的程式 ‧Create的配件包括一個藍牙存取模組（BAM），用來作無線通訊
‧http://store.irobot.com/shop/index.jsp?categoryId=3311368

## Slide 157: iRobot Create (2)
Bluetooth Adaptor Module (BAM)
  Up to 300ft (100m) range in a typical residential home (attainable range will depend on the environment)
  Wireless control of the iRobot Createý from any Windows or Linux PC or Macintosh computer
  20 pin I/O connector for adding your own hardware and sensors to the robot in addition to the wireless connection
  High power Class 1 Bluetooth radio
  Bluetooth Serial Port Profile (SPP)
  DB-25 male connector plugs into the Createýs expansion port
  Providing a virtual serial port connection between the computer and the Create robot
Notes: iRobot Create ( 2 )
‧藍牙轉接模組（BAM）
  –在一個典型的住宅中範圍可達300英尺（100米）（可達範圍取決於環境） –不論是Windows、Linux還是麥金塔電腦，皆可透過它們來無線控制iRobot Createý
  –除了無線連接，也可透過20針I / O接口在機器人上添加您個人的硬體和感測器 –高功率Class 1藍牙無線電
  –藍牙序列連接埠設定檔（SPP） –DB-25插頭插在Createýs的擴展埠 –在電腦和Create機器人之間提供一個虛擬的序列埠連接

## Slide 158: iRobot Create (3)
iRobot Create Open Interface
The Create Open Interface (OI) consists of an electronic interface and a software interface for controlling Create’s behavior and reading its sensors. The electronic interface includes a 7 pin Mini-DIN connector and a DB-25 connector in the Cargo Bay for connecting hardware and electronics for sensors and actuators such as a robotic arm or light sensor to Create.
The software interface lets you manipulate Create’s behavior and read its sensors through a series of commands including start commands, mode commands, actuator commands, demo commands, song commands, input commands, script commands, and wait commands that you send to Create’s serial port by way of a PC or microcontroller that is connected to the Mini-DIN connector or Cargo Bay.
Notes: iRobot Create ( 3 )
iRobot Create開放式介面 ‧Create開放式介面（OI）包含電子介面和軟體介面，用來控制Create的行為以及讀取其感測器。
電子介面包括一個7針Mini-DIN連接器和在Cargo Bay上的一個DB- 25連接器，用來在Create上連接硬體和感測器、執行器等電子產品，如機器人手臂或是光線
感測器。
‧軟體介面讓您經由一系列的命令來操作Create的行為，並讀取它的感測器。
命令包括啟動命令、模式命令、執行命令、演示命令、唱歌命令、輸入命令、腳本命令和等待命令。
經由一台連接到Mini-DIN連接器( 或Cargo Bay )的電腦( 或是微控制器 )，您可以發送命令到Create的序列埠。